## Slide 1: WF on core part maintenance of CSI-RS based L3 measurement requirements
Apple, …
3GPP TSG-RAN WG4#98-bis-e Meeting R4-210xxxx
Electronic Meeting, Apr. 12-20, 2021 Document for: Approval
Agenda item: 5.7.1

## Slide 2: Way forward – Scheduling restriction for intra-f CSI-RS measurement in TDD band
  When UE performs CSI-RS intra-frequency measurements in a TDD band, UE is not expected to transmit PUCCH/PUSCH/SRS on configured CSI-RS resource symbols, and on 1 OFDM symbol before and after each consecutively configured CSI-RS symbols.
    1 OFDM symbol before the configured CSI-RS symbol can leave some margin to accommodate timing error and TA uncertainty between NW and UE

## Slide 3: Way forward – Time domain restriction for CSI-RS configuration
All L3 CSI-RS resources in the same MO have identical periodicity.
For inter-frequency measurements, Rel-16 L3 CSI-RS requirements are defined under assumption that all CSI-RS resources in the same MO are configured in the same 5ms window
For intra-frequency measurements: Rel-16 L3 CSI-RS requirements are defined under assumption that CSI-RS resources in the same MO can be configured in up to two separated 5ms windows during one CSI-RS resource period.
  When intra-frequency L3 CSI-RS are configured in two separated windows, the minimum periodicity of the configured CSI-RS resources is 20ms.

## Slide 4: Way forward – Starting point of 5ms time window
For CSI-RS based L3 intra-frequency measurement, the starting point of the 5ms window is the slot boundary of the serving cell, where the corresponding slot contains the first configured L3 CSI-RS resource of the serving cell in the intra-frequency MO.
  Since it is not guaranteed that all configured L3 CSI-RS resources of the neighbor cell are always detectable for UE, the starting point can only be based on serving cell’s configured L3 CSI-RS resources.
  the definition of the starting point of 5ms window should be specified to avoid the ambiguity between NW and UE.
For CSI-RS based L3 inter-frequency measurement, there is no need to specify the starting point of 5ms window since all the measurement are MG based

## Slide 5: Way forward – UE behavior when the timing offset exceeds the threshold
  In R16 with single FFT assumption,
    For intra-frequency measurement, the UE is not required to measure the configured CSI-RS resources of a neighbour cell if the symbol level misalignment between serving and the corresponding neighbour cell exceeds the threshold.
    For inter-frequency measurement, UE can pick up any cell as the reference cell per frequency layer. UE is not required to measure the configured CSI-RS resources of a neighbour cell if the symbol level misalignment between the reference cell and the corresponding neighbour cell belonging to the same frequency layer exceeds the threshold.
  For UE which is not subject to single FFT limitation, it is up to UE how to handle the CSI-RS resources when timing offset exceeds the threshold.

## Slide 6: Way forward – Time validity of the detected associatedSSB
  Adding the definition of detected associatedSSB in 9.10.2.5 section: The associatedSSB is detected if it has been meeting the relevant cell identification requirement during the last 5 seconds.