## Slide 1: WF on further RRM enhancement for NR and MR-DC - PUCCH SCell activation/deactivation requirements
CATT
3GPP TSG-RAN WG4 Meeting #98bis-e R4-21XXXX Electronic Meeting, 12th – 20th April, 2021
Agreement in 1st round
Agreement in GTW (Apr. 16th)
Agreement in 2nd round

## Slide 2: Sub-topic 1-1 General(1/5)
Issue 1-1-1: The ending point of PUCCH SCell activation?
  The ending point for valid TA case:
    Option 1:
      For valid TA case, the ending point of PUCCH SCell activation should be the point when UE transmit valid CSI report on target PUCCH SCell.
    Option 2:
      For valid TA case, the ending point of PUCCH SCell activation is the point when UE transmit valid CSI report on a certain cell (SpCell or PUCCH SCell or others, i.e. not to define which cell is used).
  The ending point for invalid TA case:
    Option 1:
      For invalid TA case, the ending point of PUCCH SCell activation should be the point when UE transmit valid CSI report on target PUCCH SCell.
    Option 2:
      For invalid TA case, the ending point of PUCCH SCell activation is the point when UE transmit valid CSI report on a certain cell (SpCell or PUCCH SCell or others, i.e. not to define which cell is used).
    Option 3:
      For invalid TA case, the ending point of PUCCH SCell activation should be the point when UE transmit PRACH on target PUCCH SCell.
    Option 4
      Depends on if the UE has transmitted the CSI reporting e.g. to inform network the beam information during the activation period.
Issue 1-1-2: Which cell is the CSI reporting transmitted for PUCCH SCell activation?
  Closed, can be included in the discussion of issue 1-1-1

## Slide 3: Sub-topic 1-1 General(4/5)
Issue 1-1-3: Whether the beam information (SSB index) of PUCCH Scell is needed to be indicated to NW?
  Option 1: (vivo, Apple, ZTE)
    For the unknown case, the beam information of the PUCCH Scell being activated should be indicated to NW.
    For the known case, this indication of this information can be omitted.
  Option 2: (NEC)
    Needed for unknown FR1 Scell activation
      For an unknown FR1 Scell activation where CSI reporting is transmitted on Scell, RAN4 to consider including L1-RSRP/beam reporting as part of the Scell activation procedure.
  Option 3: (Nokia)
    Needed for unknown PUCCH Scell in FR2.
    Not needed for PUCCH Scell in FR1 or known PUCCH Scell in FR2.
    If RAN4 agrees to send beam information on Pcell, send LS to RAN1/2 asking for the feasibility and potential solutions of transmitting CSI report of PUCCH Scell on the Pcell.
  Option 4: (Apple, Huawei, ZTE, NTT DOCOMO, OPPO, QC)
    If the being-activated PUCCH Scell is known, no need to indicate the beam information to network for determining the associated SSB in PDCCH order for RA, i.e., no additional SSB based beam measurement is needed.
    If the being-activated PUCCH Scell is unknown:
      if target Scell belongs to FR2 and if there is at least one active serving cell on that FR2 band: following the same conditions in TS38.133 section 8.3.2 for intra-band FR2 Scell activation, no need to indicate the beam information to network for determining the associated SSB in PDCCH order for RA.
      if target Scell belongs to FR2 and if there is no active serving cell on that FR2 band: need to indicate the beam information to network for determining the associated SSB in PDCCH order for RA.
      if target Scell belongs to FR1 and it is contiguous to an active serving cell in the same band: following the same conditions in TS38.133 section 8.3.2 for intra-band contiguous FR1 Scell activation, no need to indicate the beam information to network for determining the associated SSB in PDCCH order for RA.
      if target Scell belongs to FR1 and if there is no contiguous active serving cell on that FR1 band: need to indicate the beam information to network for determining the associated SSB in PDCCH order for RA.
  Option 4a: (QC)
    The clarification for option 4:
      “need to indicate the beam information to network for determining the associated SSB in PDCCH order for RA” doesn’t necessarily mean it is always possible for all cases, i.e. there can be cases where DL beam (SSB index) indication can’t be reported to the serving cell due to UE behavior for PUCCH grouping specified by RAN1/2.

## Slide 4: Sub-topic 1-1 General(4/5)
Cont. from last page
Issue 1-1-3: Whether the beam information (SSB index) of PUCCH Scell is needed to be indicated to NW?
  Option 5: (Ericsson)
    RAN4 to focus on deriving PUCCH Scell activation requirements for the scenario where the beam index to be provided in the PDCCH order is known to NW beforehand.
  Option 6: (Xiaomi)
    No need to indicate the beam information to NW, and the SSB/PBCH index will be indicated in the PDCCH order which is used to determine the RACH occasion for the PRACH transmission
  Option 7: (CATT)
    Not needed for contention based random access. Needed for unknown cell in contention-free random access.

## Slide 5: Sub-topic 1-1 General(4/5)
Issue 1-1-4: Which cell is the L1-RSRP reporting transmitted for PUCCH SCell activation?
  Option 1: (Apple, ZTE, Ericsson, Nokia, MTK, NEC, CATT, QC)
    L1-RSRP report is transmitted on the SpCell if L1-RSRP report is needed.
  Option 2: (Xiaomi)
    L1-RSRP report is not needed.
Issue 1-1-5: Whether the UL spatial relation is needed for PUCCH SCell activation?
  Option 1: (CATT, Xiaomi, Nokia)
    No.
  Option 2: (Apple, Huawei, Xiaomi, ZTE, QC, Ericsson, NTT DOCOMO, OPPO, NEC)
    The UL spatial relation of PUCCH on target being-activated SCell should be considered for PUCCH SCell activation in FR2 only.
      the time uncertainty of the MAC CE for UL spatial relation activation of PUCCH in target being-activated SCell shall be defined in the baseline FR2 SCell activation delay part (Tactivate_basic). Details are FFS
  Option 3: (MTK)
    For valid TA case, the UL spatial relation is needed for PUCCH SCell
    For invalid TA case, FFS

## Slide 6: Sub-topic 1-1 General(5/5)
Issue 1-1-6: Known/unknown condition for PUCCH SCell activation?
  The known and unknown condition for Scell activation can be reused for PUCCH Scell.
Issue 1-1-7: UE capability for FR2 PUCCH SCell (de)activation requirements?
  Option 1: (Qualcomm, NTT DOCOMO)
    For UEs not supporting one of the following capabilities, FR2 PUCCH SCell (de)activation requirements are not defined.
      beamCorrespondenceWithoutUL-BeamSweeping
      beamCorrespondenceSSB-based-r16.
  Option 2: (Apple, Huawei, ZTE, OPPO, vivo, Nokia, MTK, CATT)
    Need more discussion

## Slide 7: Sub-topic 1-2 PUCCH Scell activation delay requirement for valid TA case
Issue 1-2 PUCCH Scell activation delay requirement for valid TA case
  Option 1: (Xiaomi, OPPO, CMCC, Ericsson, NTT DOCOMO, vivo, Nokia, CATT)
    Reuse the Rel-15 SCell activation delay requirement which is (( THARQ + Tactivation_time +TCSI_Reporting)/ NR slot length).
  Option 2: (Apple, Huawei, Xiaomi, ZTE, QC)
    In FR1, reuse the Rel-15 SCell activation delay requirement which is (( THARQ + Tactivation_time +TCSI_Reporting)/ NR slot length).
    In FR2, use normal SCell activation delay (i.e., (( THARQ + Tactivation_time +TCSI_Reporting)/ NR slot length);) in TS38.133 section 8.3.2 as baseline, but the time uncertainty of the MAC CE for UL spatial relation activation of PUCCH in target being-activated SCell shall be considered in the baseline Tactivation_time.
  Option 3: (MTK, NEC)
    Wait for the conclusions of other open issues.

## Slide 8: Sub-topic 1-3 The PUCCH SCell activation requirements for invalid TA case
Issue 1-3-1: The PUCCH SCell activation requirements for invalid TA case
  Option 1: (Apple, Xiaomi, OPPO, CMCC, NTT DOCOMO, vivo, MTK)
    If UE does not have the valid TA on the PUCCH SCell being activated, an additional UL synchronization procedure to obtain the valid TA shall be considered which including the following factors:
      the delay uncertainty in acquiring the first available PRACH occasion in the PUCCH SCell (T1);
      the delay for obtaining a valid TA command for the sTAG to which the SCell configured with PUCCH belongs (T2);
      the delay for applying the received TA for uplink transmission (T3)
  Option 2: (Huawei, CATT)
    Only T1 (The delay uncertainty in acquiring the first available PRACH occasion in the PUCCH SCell) need to be considered
  Option 3: (Ericsson, Nokia, NEC)
    Depending on the conclusions of other open issues. FFS.

## Slide 9: Sub-topic 1-3 The PUCCH SCell activation requirements for invalid TA case
Cont. from last page
Issue 1-3-1: The PUCCH SCell activation requirements for invalid TA case
  Option 4: (Qualcomm, ZTE)
    For known PUCCH SCell with an invalid TA, the single SCell activation requirements in terms of activation delay and interruption are defined as follows:
      Starting point of interruption window is the same as legacy SCell activation requirement
      Activation delay = legacy SCell activation delay + T1 + T2 + T3, where
        T1: the delay uncertainty in acquiring the first available PRACH occasion in the PUCCH SCell
        T2: the delay for obtaining a valid TA command for the sTAG
        T3: the delay for applying the received TA for uplink transmission
      CSI of the PUCCH SCell is reported on the SCell after T3
      For FR1, the above requirement also applies to “unknown PUCCH SCell with invalid TA” if one of the following conditions is met:
        ‘ssb-PositionInBurst’ indicates only one SSB is being actually transmitted, or
        ‘ssb-PositionInBurst’ indicates multiple SSBs and TCI indication is provided in same MAC PDU with SCell activation
      For FR2, if L1-RSRP report is followed by RRC reconfiguration for PUCCH-SpatialRelationInfo update based on the report during the activation procedure, an additional delay is expected
    For unknown PUCCH SCell with an invalid TA, the single SCell activation requirements in terms of activation delay and interruption are defined as follows:
      Starting point of interruption window is the same as legacy SCell activation requirement
      Activation delay = T0 + T1 + T2 + T3, where
        T0:
          If semi-persistent CSI-RS is used for CSI reporting,
          If periodic CSI-RS is used for CSI reporting,
        T1: the delay uncertainty in acquiring the first available PRACH occasion in the PUCCH SCell
        T2: the delay for obtaining a valid TA command for the sTAG
        T3: the delay for applying the received TA for uplink transmission
      PDCCH triggering CF-RA shall be after UE finishes processing the last activation command for TCI
      CSI of the PUCCH SCell is reported on the SCell after T3
      For FR2, if L1-RSRP report is followed by RRC reconfiguration for PUCCH-SpatialRelationInfo update based on the report during the activation procedure, an additional delay is expected
      For FR1, the above requirement applies only when none of the following conditions is met:
        ‘ssb-PositionInBurst’ indicates only one SSB is being actually transmitted, or
        ‘ssb-PositionInBurst’ indicates multiple SSBs and TCI indication is provided in same MAC PDU with SCell activation

## Slide 10: Sub-topic 1-3 The PUCCH SCell activation requirements for invalid TA case
Issue 1-3-2: the delay uncertainty in acquiring the first available PRACH occasion in the PUCCH SCell (i.e. T1)
  Option 1: (Apple, Xiaomi, ZTE, OPPO, CMCC, NTT DOCOMO, vivo, MTK, CATT)
    T1 is up to the summation of SSB to PRACH occasion association period and 10 ms. SSB to PRACH occasion associated period is defined in the table 8.1-1 of TS 38.213.
  Option 2: (QC, Ericsson, Nokia, NEC)
    FFS
Issue 1-3-3: the delay for obtaining a valid TA command for the sTAG to which the SCell configured with PUCCH belongs (i.e. T2)
  Option 1: (Apple, Xiaomi, ZTE, OPPO, NTT DOCOMO, vivo, MTK)
    T2 is the delay from slot n + (Tactivate_basic +T1)/(NR slot length) until UE has obtained a valid TA command for the target PUCCH SCell being activated. Slot n is the slot when UE received PUCCH SCell activation MAC CE.
  Option 2: (QC, Ericsson, Nokia, NEC)
    FFS
  Option 3: (CATT)
    Not needed
Issue 1-3-4: the delay for applying the received TA for uplink transmission on target PUCCH SCell being activated (i.e. T3)
  Option 1: (Apple, Xiaomi, ZTE, OPPO, NTT DOCOMO, vivo, MTK)
    T3 is the delay for applying the received TA for uplink transmission on target PUCCH SCell being activated, and greater than or equal to k+1 slot, where k is defined in clause 4.2 in TS 38.213.
  Option 2: (QC, Ericsson, Nokia, NEC)
    FFS
  Option 3: (CATT)
    Not needed

## Slide 11: Sub-topic 1-4 Interruption requirements for PUCCH SCell activation
Issue 1-4-1: Interruption requirements for PUCCH Scell activation in valid TA case
  Reuse the existing requirement for Scell activation in Rel-15.
Issue 1-4-2: Interruption requirements for PUCCH Scell activation in invalid TA case
  Option 1: (MTK)
    The interruption requirement shall include the existing requirement for Scell activation in Rel-15.
    FFS whether to introduce interruption by PRACH transmission due to different SCS.
  Option 2: (Apple, Xiaomi, ZTE, Ericsson, Nokia, NEC, CATT)
    Reuse the interruption requirement of normal Scell activation.
  Option 3: (Huawei, QC, OPPO)
    FFS after the additional delay are clearly defined

## Slide 12: Sub-topic 1-5 Applicability of PUCCH Scell activation requirements
Issue 1-5 Applicability of PUCCH Scell activation requirements
  Option 1: (Apple, Xiaomi, ZTE, OPPO, vivo, CATT)
    The PUCCH Scell activation delay requirement shall apply provided that,
      The UE has received a PDCCH order to initiate RA procedure on the PUCCH Scell within Tactivate_basic otherwise additional delay to activate the Scell is expected; and
      No interruption occurs in same FR as the target PUCCH Scell during the Scell activation procedure if UE supports per-FR MG, otherwise the PUCCH Scell activation delay can be extended, and
      No interruption occurs during the Scell activation procedure if UE does not support per-FR MG, otherwise the PUCCH Scell activation delay can be extended.
      The above interruption is caused by factor defined in TS38.133 section 8.2.1.1 for EN-DC, in TS38.133 section 8.2.2.1 for NR SA, in TS38.133 section 8.2.3.1 for NE-DC and in TS38.133 section 8.2.4.1 for NR-DC.
  Option 2: (Xiaomi, Qualcomm)
    PUCCH Scell activation requirements are applicable only to the following cases:
      the PUCCH Scell is in a different band from SpCell band
      for invalid TA, Ues capable of more than one TAG
      for unknown PUCCH Scell, TA shall be assumed invalid
  Option 3: (Ericsson)
    Delay requirements for PUCCH Scell activation shall account for additional time when PDCCH order is received outside Tactivate_basic. The additional time shall be accounted for by an expression and/or a delay component, e.g. max(Tactivate_basic, TPDCCH_order).
    Delay requirement for PUCCH Scell activation shall allow for extended time when there are additional interruptions during the activation procedure. The extended time shall be in proportion to the impact the interruption has on the activation procedure. The extended time can be captured on a general level in a sentence.
    In activation of multiple Scells with one PUCCH Scell, activation delay requirement shall apply at least for the PUCCH Scell in the event that one or more Scells have configurations that render parallel activation impossible for the UE. FFS on whether activation delay requirement also is to apply for Scells that are compatible with parallel activation with PUCCH Scell.
  Option 4: (Huawei, QC, Nokia)
    FFS after we have clear understanding on the framework.

## Slide 13: Sub-topic 1-6 Interruption requirements for PUCCH Scell deactivation
Sub-topic 1-6 Interruption requirements for PUCCH Scell deactivation
  Reuse the existing requirement for Scell deactivation in Rel-15.

## Slide 14: Sub-topic 1-7 PUCCH SCell deactivation delay requirement for activated PUCCH SCell with multiple Scells
Sub-topic 1-7 PUCCH SCell deactivation delay requirement for activated PUCCH SCell with multiple Scells
  Reuse the SCell deactivation delay requirement for activated SCell with multiple downlink SCells specified in section 8.3.8 of TS 38.133, which is (( THARQ + 3ms)/ NR slot length).