## Slide 1: WF for NR repeater RF requirements
CMCC
3GPP TSG-RAN WG4 Meeting # 98-bis-e R4-210xxxx
Electronic Meeting, 12th – 20th April, 2021

## Slide 2: Background on NR repeater
RAN#90e approved a new “New WID on NR Repeaters” with RAN4 as the responsible WG.
The objective of the WID is listed as below:
Normative work phase objective [RAN4]
Specify RF and EMC requirements for NR repeaters
Consider FR1 (FDD and TDD) and FR2 (TDD) bands
For the above objective, the leveraging of RF specifications for LTE repeater and IAB should be sought.
It is assumed that the repeater does not perform adaptive beamforming towards the UE.
It is assumed that the TDD repeater meets both BS and UE emission requirements (or the more stringent absolute level in dBm) in all slots.
The following constraint may be considered for TDD repeaters, as needed, to contain the workload associated with this project:
TX EIRP/TRP/power of Repeater not exceeding any UE power class defined in the band
Note: FR1 FDD repeaters testing is assumed to be conducted. This assumption can be revisited in RAN#91.

## Slide 3: WF on AGC/ALC related conducted requirements
  No dedicated ALC/AGC requirements are needed at least for the stationary repeater
  FFS on how to verify ALC/AGC actions. One candidate approach is to verify other key requirements e.g. power and emissions related requirements with several input power levels. Then the ALC/AGC would be implicitly tested.
  FFS about ACL/AGC requirements for moving repeater.

## Slide 4: WF on FR1 DL(access link) output power related conducted requirements
  Wait for the conclusion of NR repeater classes before the definition of output power for DL(access link). Once it is agreed to define different classes, appropriate power upper limits could be applied to.
  Option 1: Specified upper limits for all repeaters
    Further check whether these upper limits are per carrier or per passband
  Option 2: Reuse the same approach and upper limits as BS, e.g. no upper limits for WA, 38dBm and 24dBm upper limits for MR and LA respectively
    Further check whether these upper limits are per carrier or per passband
  Option 3: Reuse the same approach as BS/IAB, however, further check the upper limits, especially for those classes that don’t have such limits in BS/IAB spec
  Option 4: reuse the same approach as E-UTRA repeater, i.e. output power is based on declaration without any specified power upper limits

## Slide 5: WF on FR1 UL(backhaul link) output power related conducted requirements
  FFS on UL output power, taking following aspects into consideration
  avoiding performance degradation of other network from the point of UL co-existence
  LTE FDD repeater which is already in operation and having more output power should not be excluded from 3GPP requirements when it is converted to NR
  Relationship to LTE FDD repeater UL power
  near-far effect, which means repeater could only use the same compressed gain to amplify signal from UE far away from repeater because repeater have to compress its gain to guarantee amplified signal from nearby UE is not larger than the maximum value and then the output power could be lower

## Slide 6: WF on FR1 UL(backhaul link) output power related conducted requirements
  Candidate options for UL output power definition
  Option 1: Specified upper limits for all repeaters
  Option 2: not exceeding existing UE power class
  Option 3: exceeding existing UE power class
  Option 4: reusing the same approach as E-UTRA repeater for both TDD UL and FDD UL, i.e. output power is based on declaration without any power upper limits
  Option 5: reusing the same approach as E-UTRA repeater only for FDD UL, i.e. output power is based on declaration without any power upper limits specification
  Option 6: reusing the same approach as BS/IAB, however, further check the upper limits, especially for those classes that don’t have such limits in BS/IAB spec

## Slide 7: WF on FR1 power tolerance related conducted requirements
  Wait for the conclusion of class definitions and power limits
  FFS on whether reuse the same power tolerance requirements as E-UTRA repeater spec or not

## Slide 8: WF on FR1 ACLR related conducted requirements
  FFS on ACLR or some equivalent requirements with adjacent NR channel to match the same adjacent channel protection as NR/IAB spec.
  FFS on whether existing BS OBUE and EVM requirements could sufficiently cover ACLR requirements or not?
  The equivalent requirements may include modified OBUE requirements and absolute ACLR.
    FFS on how to set either absolute ACLR or modified OBUE or both of these two requirements as equivalent requirements. These two requirements are similar absolute metrics with narrower adjacent channel instead of the whole channel BW.

## Slide 9: WF on FR1 ACLR related conducted requirements
  FFS on ACLR with adjacent E-UTRAchannel requirements.
  It is suggested to embark on technical analysis instead of simulation at first.
  FFS on absolute requirements based on achieving same emissions power as an assumed UE/BS meeting ACLR requirements with a reference power.

## Slide 10: WF on FR1 spurious related conducted requirements
  The same spurious emission requirements as BS spec still apply to DL(access link).
    FFS on whether it could be reused for UL(backhaul link) , especially for FDD
  NR repeater spurious emission could include general spurious emission, co- location with other base stations, Co-existence with other systems in the same geographical area, Protection of BS receiver for FDD operating band, regional and regulation related requirements.
  Only Tx spurious emission is sufficient and Rx spurious emission is not necessary.

## Slide 11: WF on FR1 frequency deviation related requirements
  The frequency deviation of the output signal with respect to the input signal shall be no more than ±0.01 ppm for FR1.
  - Further consider if it’s absolute error or relative error.

## Slide 12: WF on FR1 EVM related conducted requirements
FFS on EVM
  whether to define EVM limits or based on manufacture’s declaration.
  FFS on which modulation up to 256QAM is feasible
  FFS to differentiate different modulation schemes for DL and UL respectively
  FFS on only one EVM level or more than one levels. If multiple EVM levels are agreed, the modulation schemes are based on declaration or not?
  FFS on whether to define more stringent requirements than current spec or not

## Slide 13: WF on FR1 input intermodulation related conducted requirements
Take the same approach of E-UTRAN repeater as baseline including general requirements, co-existence and co-location requirements.
FFS on whether some adjustment is necessary or not, e.g. frequency offset

## Slide 14: WF on FR1 output intermodulation related conducted requirements
Take BS Transmitter intermodulation requirement as the baseline for DL (access link) with 30dB coupling loss assumption when define interfering signal level.
FFS on output intermodulation for UL (backhaul link)

## Slide 15: WF on FR1 ACRR related conducted requirements
Take E-UTRA repeater specification as the baseline when define ACRR requirement for NR repeater.
FFS on whether consider the adjacent channel within the passband
Further consider the large NR CBW

## Slide 16: WF on FR1 out of band gain related conducted requirements
FFS on out of band gain requirements
FFS on whether take E-UTRA repeater spec as the baseline.
  FFS on whether to update assumptions considering higher output power is assumed for NR repeater
FFS on co-located out of band gain requirement.
  Which kind of co-located requirement is preferred? No requirements, optional requirements or mandatory requirements?
FFS on the necessity of co-existence simulation.
  Whether only technical analysis is sufficient
FFS on how to define coupling loss and power of another transmitter, some candidate options
  Options 1: only considering donor coupling loss as E-UTRA repeater spec
  Option 2: Base on assumed MCL to another transmitter with the same output power as a BS

## Slide 17: WF on FR1 TDD OFF related conducted requirements
FFS on TDD OFF requirements
Further discussion on whether TDD OFF requirements are necessary
Further discussion on how to define these requirements. One candidate option is verifying these requirements with synchronization or switching time requirements.

## Slide 18: WF on FR1 REFSENSE or equivalent conducted requirements
FFS on REFSENSE or equivalent conducted requirements
  FFS on whether these requirements are needed or not
  The candidate requirements include
    NF
    Minimum input value

## Slide 19: WF on FR2 DL(access link) power related requirements
At least define TRP requirements for FR2 repeater.
  FFS on EIRP requirements
Output power for FR2 repeater is based on declaration without upper limit in DL(access link)
TRP accuracy requirement for DL(access link) should be the same as BS spec
  FFS on conformance test.

## Slide 20: WF on FR2 UL(backhaul link) power related requirements
FFS on FR2 UL(backhaul link) output power in terms of TRP , taking following aspects into consideration
based on declaration without upper limit or not

## Slide 21: WF on FR2 ALC related requirements
FFS on FR2 ALC requirements, taking following aspects into consideration
whether to implicitly specify ALC requirements or not
ALC may be only needed in context of limiting maximum output power, unwanted emissions and output signal quality with high-power input signal that leads to gain limits

## Slide 22: WF on FR2 ACLR or some equivalent requirements
  FFS on relative ACLR or some equivalent requirements to match the same adjacent channel protection as NR/IAB spec.
  FFS on whether existing BS OBUE and EVM requirements could sufficiently cover ACLR requirements or not?
  The equivalent requirements may include modified OBUE requirements and absolute adjacent channel emissions power.
    FFS on how to set either absolute ACLR or modified OBUE or both of these two requirements as equivalent requirements. These two requirements are similar absolute metrics with narrower adjacent channel instead of the whole channel BW.

## Slide 23: WF on FR2 Tx spurious requirements
  At least for DL, the same spurious emissions requirements as BS could be reused for NR repeater including category A/B and protection of ESS.
    FSS on whether these same requirements could still apply to UL?
  Rx spurious emission is not necessary for FR2 repeater.

## Slide 24: WF on FR2 frequency deviation requirements
  The frequency deviation of the output signal with respect to the input signal shall be no more than [±0,01] PPM for FR2.
  - Further consider if it’s absolute error or relative error.

## Slide 25: WF on FR2 out of band gain requirements
  FFS on out of band gain, taking following aspects into consideration
  deployment scenarios and expected repeater gain etc.
  FFS on whether only reasonable analysis is sufficient or extra simulation is also required.

## Slide 26: WF on FR2 EVM requirements
  FFS on FR2 EVM definition, taking following aspects into consideration
  whether explicitly define EVM limits or based on manufacture’s declaration.
  which modulation up to 256QAM(DL) and 64QAM(UL) is feasible
  whether to differentiate different modulation scheme for DL and UL respectively
  only one EVM level or more than one level. If multiple EVM levels are agreed, the modulation schemes are based on declaration or not?
  whether to define more stringent requirements than current spec or not

## Slide 27: WF on FR2 input IMD requirements
  FFS on input IMD
  Further check whether to define input IMD for FR2
  Further check whether this requirement could be based on FR2 BS receiver intermodulation

## Slide 28: WF on FR2 output IMD requirements
  FFS on output IMD
  Further check whether to define output IMD for FR2