## Slide 1: 3GPP TSG-RAN WG4 Meeting #98-bis-e Electronic Meeting, April 12th – 20th April, 2021
Huawei, HiSilicon
Way forward on NR-U BS demodulation requirements
R4-2106010

## Slide 2: Test applicability rules for PUSCH/PUCCH
For each subcarrier spacing declared to be supported, the tests for a specific channel bandwidth shall apply only if the BS supports it (see D.xx in table 4.6-1). Unless otherwise stated, for each subcarrier spacing declared to be supported, the tests shall be done only for the widest supported channel bandwidth. If performance requirement is not specified for this widest supported channel bandwidth, the tests shall be done by using performance requirement defined for 20MHz channel bandwidth.
    For 15kHz SCS:
      For PUSCH test and PF0, PF1, PF2 test, the tested RB’s are uniformly spaced over the channel bandwidth at RB index {0, 10, …, 100} or {110, 120,…, 210}
      For PF3 test, the tested RB’s are uniformly spaced over the channel bandwidth at RB index {0, 10, …, 90} or {110, 120,…, 200}
    For 30kHz SCS:
      For PUSCH test and PF0, PF1, PF2 test, the tested RB’s are uniformly spaced over the channel bandwidth at RB index {55, 60,…,105}
      For PF3 test, the tested RB’s are uniformly spaced over the channel bandwidth at RB index {55, 60,…,100}

## Slide 3: CG-UCI requirements
  BetaOffsetCG-UCI-index configuration
  BetaOffsetCG-UCI-index = 8
  Number of CG-UCI information bits
  18 bits
  Pattern of CG-UCI information bits
  Use a bit pattern {c0,c1,…,c17} that consists of :
    HARQ process number: [c0,c1,c2,c3] = [0 0 0 1]
    RV sequence: [c4,c5] = [0 0]
    NDI: [c6]
      Option 1: [c6] = [1]
      Option 2: [c6] = toggle for every new transmission, e.g. 0 for even transmissions and 1 for odd ones
    COT sharing information field: [c7,c8,…c17] = [0,0,0,0,0,0,0,0,0,0,0]

## Slide 4
Parameter |  | Value
Channel model |  | TDLA30-10 Low
Bandwidth |  | 20MHz
Transform precoding |  | Disabled
Default TDD UL-DL pattern |  | 30 kHz SCS:7D1S2U, S=6D:4G:4U 15 kHz SCS: 3D1S1U S=10D:2G:2U
MCS |  | MCS 20
HARQ | Maximum number of HARQ transmissions | 1
 | RV sequence | 0
DMRS | DM-RS configuration type | 1
 | DM-RS duration | Single-symbol DM-RS
 | Additional DM-RS position | pos1
 | Number of DM-RS CDM group(s) without data | 2
 | Ratio of PUSCH EPRE to DM-RS EPRE | -3 dB
 | DM-RS port(s) | {0}
 | DM-RS sequence generation | NID0=0, nSCID=0
Time domain resource assignment | PUSCH mapping type | A, B
 | Start symbol | 0
 | Allocation length | 14
Frequency domain resource assignment | RB assignment | 1 interlace
 | Frequency hopping | Disabled
Code block group based PUSCH transmission |  | Disabled
Test metric |  | SNR@1% BLER of CG-UCI
UCI | Number CG-UCI information bits | 18
 | Scaling | 1
 | betaOffsetCG-UCI index | 8
 | UCI partition for frequency hopping | Disabled
Simulation assumptions for CG-UCI

## Slide 5: PUCCH requirements
  Test metric for PF3
  Prob(DTX->ACK)<=1% and Prob(ACK miss)<=1%
  Pattern of information bits
  PF0: [0] including HARQ-ACK information only
  PF1:[0 1] including HARQ-ACK information only
  PF3: [0 0 0 0] including HARQ-ACK information only
  Pattern of PF2 information bits
  Random information bits selection

## Slide 6: PRACH requirements
BS declaration for extended PRACH formats
[D.111] | PRACH format with LRA = 1151 for 15kHz SCS and LRA = 571 for 30kHz SCS | Declaration of the supported PRACH format(s) as specified in TS 38.211 [17], i.e., format: A2, B4, C2. Declaration of the supported SCS(s) per supported PRACH format as specified in TS 38.211 [17], i.e., 15 kHz, 30 kHz or both.

## Slide 7: Final Performance Requirements
Company is encouraged to provide both ideal simulation results and impairment results for PUSCH, CG-UCI, PUCCH and PRACH in next RAN4#99-e meeting (May)
Performance requirements will be derived as per the rules used for NR Rel-15 BS performance requirements definition (R4-1904713)
  The template for the summary of simulation results implemented this rules
Formal CRs that capture derived SNR with [ ] will be agreed in next RAN4#99-e meeting (May)
  Refer to R4-2106134 for CR splitting
Target to remove [ ] in upcoming RAN4#100-e meeting (August)