## Slide 1: Way forward on UE/BS demodulation on NR 47GHz band
Ericsson
3GPP TSG-RAN WG4 Meeting #98-bis-e
Electronic meeting, 12 – 20 April 2021
Agenda item: 7.27.4.2, 7.27.4.3
Document for: Approval
R4-2106090

## Slide 2: Agreements for UE demodulation requirements on NR 47GHz band
Extension of the applicability of the requirements are independent from the ongoing Rel-17 SI Study on enhanced test methods for FR2 UEs.
  If necessary, RAN4 FR2 EU demodulation and CSI requirements applicability could be re-visited after the conclusion of Rel-17 Testability SI.
Whether the existing UE performance requirements applicable for 47GHz band or not
  Extend the applicable FR2 operating bands up to 48200MHz for Rel-15/16 FR2 UE demodulation requirements except for 256QAM Rank 1, 64QAM Rank 2, and 16QAM Rank 1 with Enhanced Receiver Type 1.
  Interested companies are encouraged to provide the evaluation results whether the UE demodulation requirements of 64QAM Rank 2 (TS38.101-1 Table 7.2.2.2.1-4 Test 2-6) are applicable for 47GHz band without any margin or with 1dB margin
  Interested companies are encouraged to provide the evaluation results whether the following UE demodulation requirements are applicable for 47GHz band:
    256QAM Rank 1 (TS38.101-1 Table 7.2.2.2.1-3 Test 1-4 )
    16QAM Rank 1 with Enhanced Receiver Type 1 (TS38.101-1 Table 7.2.2.2.1-5 Test 3-1).
  Phase noise model from TR 38.803 Example 2 is a baseline assumption for evaluation.
    Other phase models are not precluded for the evaluation.
  For evaluation, different compensation techniques are up to UE implementation.

## Slide 3: Agreements for BS demodulation requirements on NR 47GHz band
Applicability of FR2 BS demodulation requirements
  The existing FR2 BS demodulation requirements are applicable for 47GHz band.
Test feasibility
  RAN4 assumes OTA link budget as sufficient if AWGN_offset can be chosen.
  Add the following note in the Tables ‘AWGN power level at the BS input’ for BS type 2-O in TS38.141-2 (from Rel-17 specification):
    Note X: The AWGN power level contains an AWGN offset of 15dB. If needed for test purposes, the AWGN level can be reduced by any value in the range 0dB to 15dB. Changing the AWGN level does not impact the validity of the test, as it reduces the effective base band SNR level.
  RAN4 will agree to add a similar note for FR1 BS, i.e., 38.141-1, 38.141-2, 37.145-1, 37.145-2 and 37.141 in the maintenance or in WI NR_perf_enh2_Demod.
    Add the note from Rel-17 specification
    For FR1 BS, the AWGN level can be reduced by any value in the range 0dB to 16dB.