## Slide 1: Way forward on adding 25 MHz channel BW to band n5
AT&T
­­­3GPP TSG-RAN WG4 Meeting #99-e R4-2107817
Electronic Meeting, 19th – 27th May, 2021

## Slide 2: Background
Way forward in [1] approved at RAN4 #98bis-e
Additional contributions submitted by Apple, Qualcomm, and Skyworks at RAN4 #99-e in [2], [3], and [4]
Summary of REFSENS proposals for TX/RX 20MHz/25MHz from companies based on middle-case and best-case scenarios were presented in [1]

## Slide 3: WF on UL Channel BW
Issue 4-1: UL channel BW restricted to 20MHz
Observations:
  Moderator Summary of 1st round: “25MHz has low support. It’s better to consider 20MHz only in UL to make some progress.”
WF
  Agree on asymmetric UL/DL CBW with UL BW limited to 20MHz

## Slide 4: WF on Asymmetric UL Channel Location
Issue 4-3: Additional updates if asymmetric channel BW
Observations:
  Common view on UL channel location is important to confirm
  Three scenarios for the 20MHz UL channel location:
    Worst-case: closest to the DL band
    Middle-case: middle of the UL band preserving existing duplex offset
    Best-case: farthest from the DL band
  Worst-case to be avoided due to impact on MSD
WF
  Decide on UL channel location scenario by next RAN4 meeting.
    Option 1: Middle-case
    Option 2: Best-case
  Complete the necessary updates to 38.101-1 to define the asymmetric channel location based on the agreed option by the next RAN4 meeting.

## Slide 5: Way Forward on REFSENS
Issue 4-2: REFSENS and RB allocation
Observations:
  REFSENS proposals for TX/RX 20MHz/25MHz from companies based on middle-case and best-case scenarios have been presented in [1], [2], [3], and [4]
  REFSENS proposals for TX/RX 20MHz/25MHz based on middle-case scenario from four companies relatively aligned
  UL RB allocation agreed in [1] to be close as possible to the downlink operating band within the 20MHz UL channel location
  Important to ensure that the REFSENS dataset used in REFSENS calculation follows the same assumptions
WF
  Agree on REFSENS for n5 TX/RX 20MHz/25MHz at the next meeting based on agreement on UL channel location. Possible options:
    Option 1: REFSENS based on average (in dB) based on company proposals within 3dB delta
    Option 2: REFSENS based on average (in dB) based on all company proposals
    Option 3: Others …

## Slide 6: References
R4-2105362, “Way forward on the introduction of 25 MHz in band n5”, AT&T, 3GPP TSG-RAN WG4 Meeting #98-bis-e
R4-2109449, “MSD calculation for band n5 with 20 MHz UL BW”, Apple Inc., 3GPP TSG-RAN WG4 #99-e
R4-2111467, “R17 BWs REFSENS”, Qualcomm Incorporated, 3GPP TSG-RAN WG4 #99-e
R4-2111532, “n5 25MHz REFSENS”, Skyworks Solutions Inc., 3GPP TSG-RAN WG4 #99-e