## Slide 1: WF for possible improvements on MSD in relation to BCS4
Huawei, HiSilicon
3GPP TSG-RAN WG4#99-e R4-2107822
Electronic Meeting, May 19 – 27, 2021

## Slide 2: Background
Based on the approved WF [1], RAN4 need to consider how to improve the MSD due to harmonic interference and cross band isolation. In this meeting, companies provided some analysis [2] [3] to further specify the MSD using reasonable and bandwidth-agnostic method.

## Slide 3: WF on MSD due to harmonic interference
It's proposed to choose one test configuration for MSD due to harmonic interference. And the principles are shown below.
  #1 The minimum CBW should be chosen for DL victim band
  #2 The victim's RX CBW entirely overlaps the aggressor's UL harmonic
  #3 To specify the aggressor’s UL RB allocation so that the UL harmonic is entirely contained within the victim’s smallest Rx CBW
  #4 For the case of partial overlap or near miss cases, its is necessary to ensure UL and DL carrier frequencies are specified.
RAN4 can further study how to specifically improve the MSD test table due to harmonic interference in next meeting.

## Slide 4: WF on MSD due to cross band isolation
There are three cases to be considered for different UL Tx bandwidths, DL Rx bandwidths and frequency gap between UL and DL carrier frequencies
  Case 1: Tx ACLR1 is overlapping with the Rx DL channel.
  Case 2: Tx ACLR2 is overlapping with the Rx DL channel without Tx ACLR1 overlapping.
  Case 3: Others: the Rx CBW is neither victim of the aggressor’s Tx ACLR1 nor of the Tx ACLR2.
For case 3, MSD test configuration can be specified as following principle.
No. | Parameters | Test configuration C
1 | Carrier Frequencies | The UL and DL carrier frequencies should be configured to minimize the gap separating the DL victim carrier to the UL carrier frequency.
2 | UL Channel bandwidth | FFS
3 | UL RB allocation | Highest possible Lcrb that is compatible with the DFT-s-OFDM 2,3,5 radix rule for the configured UL CBW, ie. fully allocated UL configuration
4 | UL SCS | NR SCS should be the smallest SCS that is compatible with the configured UL CBW
5 | DL Channel bandwidth | FFS
6 | DL RB allocation | Highest possible Lcrb that is compatible with the DFT-s-OFDM 2,3,5 radix rule for the configured DL CBW, ie. fully allocated DL configuration.
7 | DL SCS | NR SCS should be the smallest SCS that is compatible with the configured DL CBW.

## Slide 5: WF on MSD due to cross band isolation
For case 1 (e.g. CA_n1-n3) and case 2 (e.g. CA_n1-n40), the following options can be considered with UL full RB allocation.
  Option 1: For case 1 or case 2, we can choose an appropriate DL Rx channel bandwidth which only overlaps with 1st or 2nd adjacent channel in Tx aggressor band as proposed in R4-2110406.
  Option 2: To adopt fully allocated UL allocation for the highest specified UL CBW of the UL band as proposed in R4-2107322
  Option 3: Other solutions are not precluded.

## Slide 6: WF on MSD due to CIM interference
For case 1 (e.g. CA_n1-n3) and case 2 (e.g. CA_n1-n40), is it necessary to introduce MSD due to CIM interference with UL fewer RB allocation?
  Option 1: No, there is no need to introduce this kind of MSD.
  Option 2: Yes, to introduce MSD due to CIM interference for inter-band CA as proposed in R4-2110406.
  Option 3: Other solutions are not precluded.

## Slide 7: References
# | TDoc | Title | Source
1 | R4-2105373 | Possible improvements on MSD in relation to BCS4 | Huawei, HiSilicon, Skyworks Solutions Inc.
2 | R4-2110405 | Discussion on how to simplify MSD due to harmonic interference using bandwidth-agnostic approach | Huawei, HiSilicon
3 | R4-2110406 | Discussion on MSD due to cross band isolation and counter intermodulations | Huawei, HiSilicon