## Slide 1: WF on RedCap
Ericsson
R4-2108005
3GPP TSG-RAN WG4 Meeting # 99-e
Electronic Meeting, May 19-27, 2021

## Slide 2: RedCap: General issues
RedCap bands:
  Any FDD or TDD band could support RedCap.
RedCap UE Power Class
  Existing PC per band could be considered.
    PC3 should be prioritized if needed.

## Slide 3: RedCap: BS RF impact
No BS RF impact is expecting when introducing RedCap.

## Slide 4: RedCap: Rx branch for RedCap UE
FR1
  Minimum # of Rx branch to be specified: 1
  Additional # of Rx branch to be specified: 2
FR2:
  FFS
    Operators are encouraged to provide feedback on use case of RedCap UE in FR2 for next meeting, e,g Power class, frequency band etc.

## Slide 5: RedCap: FR1 UE Tx-Rx and Rx-Tx switching time
Tx-Rx switching time: 13 µs
Rx-Tx switching time: FFS
  Companies are encouraged to provide their analysis justifying any longer switching time than 13 µs
  Study network performance impact and trade-off with UE power savings

## Slide 6: RedCap: UE RF impact
Tx requirements
  NR UE Tx requirements could be reused for RedCap (except the UE transmit power in FR1 and FR2)
  Transmit power in FR1 and FR2: depend on the RedCap PC and frequency band.
Rx requirements:
  Specify REFSENS:
    For one Rx branch.
    For 2 Rx branches for bands where legacy NR UE is required with 4 Rx antenna ports.
    re-use existing single carrier requirement for 2 Rx branches, FFS on HD-FDD mode.
  Other requirements: FFS
Specification structure:
  Define new suffix for RedCap UE RF requirement at least in TS 38.101-1.

## Slide 7: RedCap: RRM eDRX RF
No impact on eDRX RF

## Slide 8: References
R4-2109675, General views on Redcap UE RF requirements, Vivo
R4-2109683, Discussion and reply LS on Half-duplex FDD switching time for RedCap UE, Vivo
R4-2109747, On the scope of work on RF core requirements Redcap, Nokia, Nokia Shanghai Bell
R4-2109879, Draft Reply LS on Half-duplex FDD switching time for RedCap UE, Huawei, HiSilicon
R4-2109880, General discussion for RedCap UE, Huawei, HiSilicon
R4-2111196, RAN4 RF WI work plan for RedCap, Ericsson
R4-2111197, RF impact analysis on R17 RedCap, Ericsson
R4-2111198, Reply LS to Half-duplex FDD switching for RedCap UE, Ericsson
R4-2111424, RedCap RF Issues, Qualcomm