## Slide 1: WF on NR repeaters EMC requirements
ZTE, [...]
3GPP TSG-RAN WG4 Meeting # 99-e
Electronic Meeting, May. 19-27, 2021
R4-2108479
Agenda item: 9.5.4
Document for: Approval

## Slide 2: Background
A new TS (TS38.114) was agreed for NR Repeaters EMC according to the revised WID for NR repeaters (RP-210818).
Some the NR FDD/TDD repeaters EMC requirements are discussed in 1st round email discussion

## Slide 3: WF(1)
For the time being, only focus core requirement for TDD and FDD NR repeater EMC.
The following EMC requirements are referred to CISPR or IEC specifications and can be applied to NR FDD/TDD repeaters
  Radiated emission(ancillary equipment), conducted emission (including DC power input/output port, AC mains power input/output port, Telecommunication port) , Harmonic current emissions(AC mains input port), Voltage fluctuations and flicker (AC mains input port)
  RF electromagnetic field (80 MHz to 6000 MHz), conducted immunity (0.15 MHz - 80 MHz), ESD, EFT, Voltage dips, surges
For “exclusion bands” requirements, it is premature to decide, pending on the repeater RF discussion

## Slide 4: WF(2)
Other than the requirments in previous slide, other requirements (such as radiated emission requirement) for NR TDD repeaters are pending on the repeater RF discussion, more discussions are needed for TDD NR repeaters
Other than the requirments in previous slide, other requirements (such as radiated emission requirement) for NR FDD repeaters use TS 36.113 and TS 38.113 as a starting point

## Slide 5: WF(3)
Issue 4-2-2: For test conditions, performance assessment and performance criteria, whether or not TS 36.113/TS38.113 can be directly reused for NR repeaters especially for TDD?
  Option 1: Yes, can be directly reused for both NR FDD and TDD repeaters EMC
  Option 2: No, can be directly reused for NR FDD repeaters EMC, but not for NR TDD repeaters EMC
  Option 3: No, It is premature to decide, pending on the repeater RF discussion, more discussions are needed for TDD NR repeaters.
Recommended WF： Option 3
Issue 4-2-3: If EMC requirements (core and performance) are the same for all the repeater classes for both FDD and TDD repeaters, namely WA, MR, LA and home class?
  Option 1: Yes
  Option 2: No
  Option 3: It is premature to decide, pending on the repeater RF discussion, especially for performance.
Recommended WF： Option 3.

## Slide 6: References
R4-2108428, 1st round summary for [99-e] [303] NR_EMC, ZTE Coporation
R4-2109652, Further discussion on NR repeaters EMC, ZTE Coporation
R4-2110044, Discussion on EMC requirements for NR Repeater, Ericsson
R4-2111464, Analysis of the NR repeater implementation into the existing NR BS EMC specification TS 38.113, Huawei