## Slide 1: WF on BS TX RF requirements for 52.6 – 71 GHz
Nokia
3GPP TSG-RAN WG4 Meeting # 99-e
Electronic Meeting, 19 – 27 May 2021
Agenda Item: 9.15.5
R4-2108638

## Slide 2: Background
Contributions on BS RF TX requirements for 52.6 – 71 GHz in RAN4#98-bis-e have a variety of proposals:
[1] R4-2109114 Discussion on BS TX RF requirements for 52 6-71GHz CATT
[2] R4-2109384 Proposals on BS transmitter requirements for extending current NR operation to 71 GHz Nokia, Nokia Shanghai Bell
[3] R4-2109870 On BS RF transmitter requirements for the frequency range 52 to 71 GHz Ericsson
[4] R4-2110601 Discussion on BS Tx requirements for 60GHz ZTE Corporation
The Way Forward from the discussion of the contributions are summarized in the following slides.

## Slide 3: Way forward on General and output power requirements
Re-use FR2 EIRP accuracy as baseline.
  Proponents of new EIPR accuracy limits (other than the current FR2 ones) should provide technical justifications in next RAN4 meeting.
Re-use fractional bandwidth concept from current FR2.
  Further study whether 6% is correct breakpoint for fractional bandwidth.
Re-use OFF power requirement of -36 dBm/MHz from FR2.
Consider transient period together with transmit OFF power, and also together with UE requirement.
  For information, no agreement was reached in 1st round to change UE transient period.
Total power dynamic range requirement is based on 10*log10(Nrb) for all SCS and ChBW.

## Slide 4: Way forward on Timing and signal quality requirements
Study CA TAE and MIMO TAE further.
  Proponents of new CA TAE and MIMO TAE limits (other than the current FR2 ones) should provide technical justifications (e.g., preliminary simulation results) in next RAN4 meeting.
Consider BS type 2-O EVM requirements, but allow further time to check.
  Proponents of new EVM limits (other than the current FR2 ones) should provide technical justifications (e.g., preliminary simulation results) in next RAN4 meeting.

## Slide 5: Way forward on Emission requirements
Apply FR2 approach for spurious emissions, with necessary adaptations to emissions mask step frequencies.
Occupied bandwidth measurement step size postponed to performance part.
FFS for low emission PSD.
  Depending on decision of the OBUE.
FFS for ACLR.
  Depending on decision (together with UE side) on whether new simulation exercise should be performed.
FFS for OBUE.
  First discuss and decide on OBUE for unlicensed operation where regulatory requirements in Europe are clear.