## Slide 1: WF for eMTC RF requirements
NTT DOCOMO, INC.
R4-77AH-IoT-0058
3GPP TSG-RAN WG4 Meeting #77 NB-IOT AH
Budapest, Hungary, 20 – 22 Jan, 2016
Agenda Item: 4.2
Source: NTT DOCOMO, INC.
Title: WF for eMTC RF requirements
Document for: Approval

## Slide 2: Introduction
In R4#77, reusing the existing ACLR and SEM for 1.4 MHz channel bandwidth was proposed regardless of practical system bandwidths set by eNB.
In our understanding, the requirements would be unnecessarily tighter and require more MPR from co-existence perspective.
In addition, it was proposed that applying the same MPR for Power Class 3 derived based on the proposed ACLR and SEM to 20 dBm power class.
  Applying the MPR from Power Class 3 may require unnecessarily larger MPR for 20dBm power class if the absolute value of SEM is the limiting factor to derive MPR.
As a result, eMTC UEs are required to use unnecessarily larger MPR. Hence, they may increase the number of transmission repetitions to complement the lost area coverage.
  Note that 3GPP has assumed 20 dBm power class to be reasonable by considering UE implementation(cost ) and coverage enhancement. Thus, if we apply more MPR to 20 dBm power class, the existing coverage may shrink or we need to pay extra cost in terms of increased number of transmission repetitions.
This contribution aims to identify reasonable definition of ACLR and SEM for eMTC to resolve the above issues.

## Slide 3: Way forward
MPR for power class 3 and 20 dBm power class shall be separately evaluated.
SEM and ACLR are proposed in slide 7, 8 and 9.
  Note UTRA ACLR 1 and 2 are FFS including their necessity
The MPR shall be based on the SEM, ACLR and in-band emission shown in slide 5, 6, 7 and 8 for each system bandwidth.
  Handling of UTRA ACLR 1 and 2 may need more discussion based on slide 9 and 10.
The 1st priority for specification work shall be 20 dBm power class.
According to the outcome of the MPR, further simplification of ACLR and SEM may be considered.

## Slide 4
Details

## Slide 5: Preconditions
When eMTC UEs are active under a network with 5, 10, 15 or 20 MHz channel bandwidth, the following channel bandwidths for UEs are considered.
  Transmission bandwidth configuration is 1.08 MHz regardless of channel bandwidths
  eMTC UEs shall be available anywhere confined within a channel bandwidth set by eNB
Channel bandwidths for NW(MHz) | Channel bandwidths for UEs(MHz)
5 | 1.58 = 1.08 + 0.25 x 2
10 | 2.08 = 1.08 + 0.50 x 2
15 | 2.58 = 1.08 + 0.75 x 2
20 | 3.08 = 1.08 + 1.00 x 2

## Slide 6: eMTC SEM and in-band emission
For each channel bandwidth, applying the existing SEM for 1.4MHz channel bandwidth.
However, handling of edges, i.e., guard bands is different from system bandwidth to system bandwidth.
Within region of transmission bandwidth and guard bands, in-band emission is applicable.
Transmission bandwidth
=1.08 MHz
- 10 dBm/30kHz
- 10 dBm/30kHz
- 10 dBm/MHz
- 10 dBm/MHz
-30dBm/MHz
-30dBm/MHz
Frequency[MHz]
The width of this region is changeable depending on system bandwidth.
For 5, 10, 15, 20 MHz, 0.25, 0.5, 0.75, 1 MHz, respectively
For this region, in-band emission is applicable since without it, it means no requirements for this regions
LO
-25dBm/MHz
-25dBm/MHz
Follow 1.4MHz SEM and general spurious
Follow 1.4MHz SEM and general spurious
1MHz
1.5MHz
0.3MHz
1MHz
1.5MHz
0.3MHz

## Slide 7: eMTC ACLR(1/2)
ACLR is 30 dB regardless of system bandwidth
However, handling of offset frequency from the center (LO) is different from system bandwidth to system bandwidth.
  See the next slide on the details
On MBW, we may adopt 4.5, 9, 13.5 and 18 MHz for victim side. However, considering SEM, it would be sufficient to check the impact of the closest area.
Transmission bandwidth
=1.08 MHz
Frequency[MHz]
The width of this region is changeable depending on system bandwidth.
For 5, 10, 15, 20 MHz, 0.25, 0.5, 0.75, 1 MHz, respectively
LO
Measurement bandwidth
Measurement bandwidth
For 5MHz system bandwidth, 1.08+0.25x2=1.58MHz
For 10MHz system bandwidth, 1.08+0.50x2=2.08MHz
For 15MHz system bandwidth, 1.08+0.75x2=2.58MHz
For 20MHz system bandwidth, 1.08+1.00x2=3.56MHz

## Slide 8: eMTC ACLR(2/2)
 | Channel bandwidth / eMTC ACLR / Measurement bandwidth |  |  | 
 | 5 MHz | 10 MHz | 15 MHz | 20 MHz
eMTC ACLR | 30 dB | 30 dB | 30 dB | 30 dB
Measurement bandwidth | 1.08 MHz | 1.08 MHz | 1.08 MHz | 1.08 MHz
Adjacent channel centre frequency offset [MHz] | +1.58 / -1.58 | +2.08 / -2.08 | +2.58 / -2.58 | +3.08 / -3.08

## Slide 9: eMTC ACLR for UTRA ACLR 1
Consideration of UTRA ACLR 1:
  Absolute value perspective
    Provided that eMTC ACLR for eMTC for 10 MHz channel bandwidth can be hold in other channel bandwidth, from absolute value perspective, the highest interference level from eMTC into UTRA ACLR 1 region is -10dBm/1.08MHz(20dBm-30dB)
    On the other hand, existing LTE ACLR for UTRA ACLR 1 provides 10dBm/3.84MHz (= 23 dBm - 33dB)
    However, from eMTC SEM perspective, the -10 dBm/1.08MHz would not significantly change even if we adopt MBW of 3.84 MHz.
    In addition, the impact of eMTC UE where the UEs uses with offset of 2.5 MHz from the edge of channel bandwidth such 5, 10, 15 and 20 MHz would not cause sever interference to adjacent UMTS UL since the maximum level is suppressed under -25dBm/MHz from SEM.
  Probability perspective
    Thus, from probability perspective, eMTC would not provide more significant interference to UMTS than LTE to UMTS as well.
Summary
  To surely protect UMTS, it would be better to have UTRA ACLR 1. On the other hand, the newly specified requirements may be able to cover it.
  Views on necessity of eMTC for UTRA ACLR 1 from other companies welcome.

## Slide 10: eMTC ACLR for UTRA ACLR 2
Consideration of UTRA ACLR 2:
  Provided that proposed SEM is satisfied, the interference level from eMTC into UTRA ACLR 2 region is quite limited and even if we define it as 36 dB, it will be easily satisfied.
  Note that -30dBm/MHz is already satisfied due to SEM. Even if MBW is extended to 3.84 MHz, 20 dBm - (-30 dBm + 5.84 dB) = 44 dB would be satisfied.
  In addition, as at least linearity of 30 dB is maintained, UTRA ACLR 2 may not be necessary.
Summary
  From technical point of view, eMTC ACLR for UTRA ACLR 2 seems not necessary.
  Views on necessity of eMTC for UTRA ACLR 2 from other companies welcome.

## Slide 11
Annex

## Slide 12: Co-existence with adjacent operators
In principle, 1.4 MHz channel bandwidth requirements assume that the adjacent operators also use 1.4 MHz channel bandwidth.
Thus, the requirements are basically tighter than those for 5, 10, 15 and 20 MHz channel bandwidth, respectively due to the smaller guard bands.
Provided that if the completely same requirements for 1.4 MHz channel bandwidth were applied to those for 20 MHz channel bandwidth, it would unnecessarily tighter requirements from co-existence with adjacent operator point of view due to the large guard band, the LO always to be the center of the transmission bandwidth and the max RBs to be 6RBs
  Note that thanks to the LO to be always the center of the transmission bandwidth, the actual noise does not reach to far distance compared to using up to 6RBs with 20 MHz CBW
Case 1:
1.4 +1.4 MHz CBW
Case 2:
20+20 MHz CBW
Case 3:
20+20 MHz CBW
inside 1.4 MHz CBW
20 MHz
20 MHz
18 MHz
18 MHz
18 MHz
18 MHz
Less impact on adjacent operators’ NW
compared to case 1
The distance b/w operators is smaller so that larger
impact on each other compared to case 3

## Slide 13: Co-existence within the same operator
If the same linearity for both LTE and eMTC is required, noise (in-band emission) within system bandwidth for eMTC is less than that for LTE.
  This comes from the fact that the LO frequency is always at the center of transmission bandwidth for eMTC so that the noise does not reach far away with higher level compared to LTE.
  The above can be clear from in-band emission requirements. Thanks to the retuning feature, the eMTC UEs would not have in-band emission due to Image outside 1.4MHz within system bandwidth.
  Note that in the below figure, general in-band emission for LTE does not reflect the exact requirements. These are subject to change according to the number of RBs, its power and so on. Also SEM, ALCR and general spurious emission for eMTC are one of the examples.
  Note that in-band emission basically is based on relative requirements compared to the power for transmission bandwidth so that it is difficult directly compare with SEM, ACLR and general spurious. However, in most cases, the constraints due to SEM, ALCR and general spurious are more stringent than those due to in-band emission within system bandwidth.
LTE
eMTC
LO
20 MHz
LO
LO leakage
image
General in band emission
SEM, ACLR , general spurious emission