## Slide 1
R4-77AH-IoT-0060
WF for NB-IOT operating bands and channel arrengements

## Slide 2: Background
This contribution captures the intial agreements for NB-IOT operating bands and channel arrengements which were endorsed in RAN4 NB-IOT Ad-Hoc in Budapest. Background information for agreements can be found from listed references.
This contribution also lists topics that needs further discussion in next meeting.
REFERENCE:
R4-77AH-IoT-0059, NB-IOT UE RF aspects, Nokia Networks

## Slide 3: NB-IOT operating bands and channel arrengements agreements
Use TS 36.101 for NB-IOT UE RF requrements
Assign suffix F for NB-IOT sub-clauses
Re-use existing E-UTRA band definition for NB-IOT. NB-IOT clause list appropriate bands and refers back to E-UTRA band definition clause.
For Standalone and guardband operation NB-IOT uplink and downlink channel bandwidth is 200 kHz for both single tone and multitone.
Channel spacing for standalone NB-IOT is 200 kHz
Channel raster for standalone NB-IOT is 100 kHz
E-UTRA Channel numbering is used for standalone NB-IOT
E-UTRA Tx-Rx frequency separationis used for standalone NB-IOT

## Slide 4: NB-IOT operating bands and channel arrengements open issues
E-UTRA Channel numbering is used for guardband and in-band NB-IOT
Tx-Rx frequency separationis used for guardband and in-band NB-IOT