## Slide 1: Way Forward on eMTC
Ericsson, Qualcomm Incorporated, Intel Corporation, CATT, Nokia Networks
R4-77AH-IoT-0148
3GPP TSG RAN WG4 Meeting #77 NB-IOT AH
Budapest, Hungary, 20-22, 2016
Agenda Item: 4.3

## Slide 2: Background
RAN4 has studied measurement requirements performance for Rel-13 MTC for the last few meetings.
Following RAN4 RRM CRs have been presented at RAN4#77 NB-IOT AH meeting.
  R4-77AH-IoT-0129: Reference configuration for Rel-13 MTC
  R4-77AH-IoT-0123: Measurement requirements for Rel-13 MTC UE under normal coverage
  R4-77AH-IoT-0125: Measurement requirements for Rel-13 MTC UE under enhanced coverage
  R4-77AH-IoT-0126: Measurement accuracy requirements for Rel-13 MTC UE
  R4-77AH-IoT-0127: Radio link monitoring for Rel-13 MTC UE
  R4-77AH-IoT-0140: RRM requirements for eMTC in IDLE mode in section 4
The purpose of this way forward document is to capture the agreements and remaining issues of eMTC work.

## Slide 3: Agreements at RAN4#77 NB-IOT AH
Cell identification:
  For cell identification for non-DRX,
    1.44s for Gap pattern 0, and
    2.88s for Gap pattern 1.
  In non-DRX, L1 periods are 480ms for Gap pattern ID 0 and 960ms for Gap pattern ID 1
No RSRQ measurement requirements in Rel-13
The number identified cells to be measured by UE for eMTC is 6 for both normal coverage and enhanced coverage.
Note: The above requirements are derived considering similar methodology used for inter-frequency measurement requirements.

## Slide 4: Agreements at RAN4#77 NB-IOT AH
RLM:
  For the normal coverage, the out-of-syn is [400]ms and in-sync [200]ms in non-DRX
    Maximum number of repetition for M-PDCCH is configurable parameter, and for out-of-sync the number is M and for in-sync the number is M-1;
  For the enhanced coverage, the numbers of time period for out-of-sync and in-sync are kept TBD in the CR.
    Maximum number of repetition for M-PDCCH is configurable parameter, and for out-of-sync the number is R and for in-sync the number is R/2;
  Aggregation level
    CEModeA: 24 for OoS and 8 for InS
    CEModeB 24 for OoS and 24 forInS

## Slide 5: Remaining work:
Resolve remaining TBDs in the CRs
  TBDs in RLM requirements for enhanced coverage needs to be resolved.
  TBDs in minimum number of ACK/NACK for SI reading requirements needs to be resolved.
Test cases for corresponding RRM requirements shall be developed.