## Slide 1: WF for NB-IoT REFSENS, repetitions and OOB
Nokia, Vodafone, Sony, Telecom Italia, Intel, NTT Docomo, Mediatek, Skyworks, Huawei, Qualcomm, CMCC

## Slide 2: WF for NB-IoT REFSENS and repetitions
REFSENS without repetitions is defined as a baseline. This REFSENS will be used as reference for other NB-IoT Rx requirements
Sensitivity with repetitions will also be defined in section 7.3.1F. This REFSENS is specified only for normal conditions. No channel model is used in the test.
Discuss the details of Repetition sensitivity in Nanjing
  How many repetitions should be used, need to know to define RMC
  What is feasible gain to be expected from repetitions
  How many channels per band needs to be tested
  AOB

## Slide 3: REFSENS Parameters
1/f noise = 0.8 dB
IM = 2.0
SNR = 1.9
NF = 8.5
 - 108.2 dBm for all bands of the WI

## Slide 4: Out of band blocking
OOB Ranges
Range 1: Current blocker levels and REFSENS +6.0 dB
Range 2: Current blocker levels and REFSENS +6.0 dB
Range 3: To be discussed in Nanjing
Range 4 : Not needed