## Slide 1: Way forward on test configuration
Nokia, Ericsson, Huawei
3GPP TSG-RAN WG4 Meeting #79AH
Hong Kong, China, 28 – 30 June 2016
R4-79AH-0264

## Slide 2: References
R4-79AH-0062, “BS conformance tests: Test strategy, Test Models and Test Configurations”, Ericsson.
R4-79AH-0181, “Proposals on Test Configurations for NB-IoT BS Testing”, Nokia, Alcatel-Lucent Shanghai Bell.
R4-79AH-0204, “Discussion on 37.141 test configuration”, Huawei.

## Slide 3: Way forward for in-band or guard-band operation
To define new TC using the current TC2, TC3, TC4 and TC5 in TS 37.141 as bases.
For guard-band operation, use 10 MHz E-UTRA carrier (or the narrowest supported E-UTRA carrier bandwidth) instead of 5 MHz E-UTRA carrier.
Place the powered boosted NB-IoT PRB as the outermost PRB at one or both edges of the BS RF bandwidth according to manufacturer declarations.

## Slide 4: Way forward for standalone operation
To define new TC using the current TC4 and TC5 in TS 37.141 as bases.
Replacing one or more GSM carrier(s) with stand-alone NB-IoT carrier(s) according to manufacturer declarations.