## Slide 1: Way forward on the same MOs configured by MN and SN
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #AH1807 Montreal, Canada, 2nd – 6th July, 2018
Agenda item: 5.2.2
R4-1809026

## Slide 2: Background
When the E-UTRA PCell and NR PSCell configure the same NR carrier frequency layer to be monitored by the UE, this layer shall be counted only once to the total number of effective carrier frequency layers, unless the configured NR carrier frequency layers to be monitored have,
  Different subcarrier spacing, or
  Different RSSI measurement resources,
  FFS different SMTC configurations or different useServingCellTimingForSync indications

## Slide 3: Way forward
Capability-wise,
  Multiple identical MOs configured from MN and SN can be counted as 1.
  MOs with different SMTC configurations cannot be counted as 1
  MOs with different absThreshSS-BlockConsolidation, nofSS-BlocksToAverage or offsetMO cannot be merged
  MOs configured to UE may lead to different behaviour due to timing information should not be merged
  Whether the UE is capable of calculating the correct SMTC configuration in order to merge MOs configured from MN and SN is up to implementation.
Since the MO is not used in the RAN4 spec, when the E-UTRA PCell and NR PSCell configure the same NR carrier frequency layer to be monitored, this layer shall be counted only once only if the UE can measure the carrier frequency with a single measurement

## Slide 4: Way forward
Considering multiple MOs that target the same frequency carrier,
  No additional UE requirements shall be defined for multiple MOs with different numerologies
  No additional UE requirements shall be defined for multiple MOs with different SMTC configurations
  UE measurement activities upon receiving multiple MOs are up to implementation