## Slide 1: Way Forward on Channel Model for NR UE Demodulation and CSI Requirements
Huawei, …
3GPP TSG-RAN WG4 Meeting AH1807
Montreal, Canada, 2 – 6 July, 2018
R4-1809359

## Slide 2: Background
RAN4#87, R4-1808028 Way forward on channel model for NR demodulation requirements was approved

## Slide 3: FR1 Channel Model
Simplification methods
  Option 1: Choose strongest paths that contribute to [X%] of total power
    Option 1: X=90% for TDL-A; X=87% for TDL-C
    Option 2: X = 90% or 95% for TDL-A and TDL-C
  Option 2: Choose 9 paths for TDL-A and TDL-C using the frequency correlation method
    TDL-A: Tap#1-6, 9, 11, 15 defined in Table 7.7.2-1 of TR 38.901
    TDL-C: Tap#1-2, 4-8, 13-14 defined in Table 7.7.2-3 of TR 38.901
Number of path: less than or equal to 12 is acceptable from test equipment point of view

## Slide 4: FR1 Channel Model
Doppler frequency and Doppler shift
  Low speed:
    TDD 10Hz (3km/h)
    [FDD 5Hz (3km/h)]
  Medium speed: 100Hz (30km/h)
  High Speed: 400Hz (120km/h)
  High speed train scenarios:
    FFS maximum Doppler shift
    Need further discussion on the channel model
    FFS SCS and CP length for high speed performance requirements
Power delay profiles and Delay spread values
  TDL-A with Delay spread RMS=30ns
  TDL-B with Delay spread RMS=100ns
  TDL-C with Delay spread RMS=300ns
  TDL-D and TDL-E can be considered in the future release if needed
MIMO correlation models
  The following models need to considered in different performance requirements
    ULA Low
    ULA medium
    X-pol low,
    X-pol Medium-A,
    X-pol spatially high

## Slide 5: FR1 Channel Models
Channel model for initial simulations
  Model #1
    TDL-A
    DS = 30 ns
    Max Fd = 10 Hz
    Low antenna correlation
  Model #2
    TDL-C
    DS = 300 ns
    Max Fd = 100 Hz
    Low antenna correlation
  Note: This is only for initial simulation alignment. The example models are not for final channel model definition and parameters can be changed.

## Slide 6: Informative for Option 2
The method can be extended to more taps. The 9 taps of the simplified model (in red) are not normalized to rms delay spread
The method can be extended to more taps. The 9 taps of the simplified model (in red) are not normalized to rms delay spread

## Slide 7: Simplified NLOS models for option 1-2

## Slide 8: Simplified NLOS models for option 1-2

## Slide 9: References
[1] R4-1808758, “Propagation channel models for UE demodulation requirements,” Intel, July 2-6, 2018
[2] R4-1808773, “Views on channel models,” NTT DoCoMo, July 2-6, 2018
[3] R4-1808803, “Demodulation performance impacts due to simplified propagation channel models,” Ericsson, July 2-6, 2018
[4] R4-1809299, “On channel model for demodulation performance requirements,” Huawei, HiSilicon, July 2-6, 2018
[5] R4-1808028, “Way forward on channel models for NR UE demodulation requirements”, Intel Corporation