## Slide 1: Way forward on OCNG pattern for RF and demodulation requirements
Rohde & Schwarz
3GPP TSG-RAN WG4 Meeting AH-1807 R4-1809395
Montreal, Canada, 02nd – 06th July 2018

## Slide 2: Background and Rational
At R4-AH-1807 meeting, R4-1808852 and R4-1808849 propose OCNG pattern for NR RF Rx testing respectively for FR1 and FR2.
The pattern descriptions follow the LTE format, where different OCNG patterns were defined for different RBs allocated with OCNG.
However the scope and result is always the same:
  all unallocated resources are filled with pseudo randomly QPSK modulated data with the same power
In addition:
  the many virtual UEs are not necessary since these would be transparent for DUT, which is assumed to demodulate only the assigned PDSCH.
  since there is no DL Tx diversity for NR, in case multiple antenna ports transmission is used, the same transmission scheme as for the DUT can be used for OCNG.
  allocation of control region with OCNG can be part of the OCNG pattern.
As such the definition of OCNG for NR can be more generic, which will decrease the maintenance work and will increase the specification readability.

## Slide 3: Proposals
1) Describe OCNG pattern in a more compact and simplified manner using following table format. Addition and/or removal of colums / rows as appropriate is not precluded.
2) Don‘t differentiate OCNG patterns based on different resources allocated with OCNG.
3) Introduction of a power coefficient scaling the OCNG power is need based.
4) The proposal is for RF, Demod and CSI. However it can be considered for RRM as well.
OCNG Appliance OCNG Parameters | Control Region (CORESET) | Data Region
Resources allocated |  | 
Structure |  | 
Content |  | 
Transmission scheme for multiple antennas ports transmission |  | 
Subcarrier Spacing |  | 
Power Level |  | 
Note 1: … |  | 
Table A.…: OP.x OCNG pattern for …

## Slide 4: Example
The following is an example how the proposed format could be used to define a generic OCNG pattern. This example is just for illustration purposes.
OCNG Appliance OCNG Parameters | Control Region (CORESET) | Data Region
Resources allocated | All unused REs (Note 1) | All unused REs (Note 1)
Structure | PDCCH | PDSCH
Content | Padding REs | Uncorrelated pseudo random QPSK modulated data
Transmission scheme for multiple antennas ports transmission | … | Spatial multiplexing using any precoding matrix with dimensions same as for RMC PDSCH
Subcarrier Spacing | Same as for RMC PDCCH | Same as for RMC PDSCH
Power Level | Same as for RMC PDCCH | Same as for RMC PDSCH
Note 1: Unused REs are REs not used by cell, beam and RMC relevant signals and channels including empty REs configured for IM purposes. |  | 
Table A.5…: OP.1 Generic OCNG pattern for full unused-resources allocation