## Slide 1: WF on test configuration for NR BS
Nokia, Nokia Shanghai Bell, Ericsson, Huawei
R4-1809463
3GPP TSG-RAN WG4 Meeting AH1807
Montreal, Canada, 2- 6 July 2018
Agenda Item: 5.1.2

## Slide 2: Background
During RAN4 AH1807 meeting test configurations were discussed in the following contributions:
R4-1808793 NR Test Configurations - remaining issues, Ericsson
R4-1808818 On typical channel bandwidth for NR test configuration, ZTE
R4-1808819 On NR OBW test configuration for Contiguous CA, ZTE
R4-1809152 On test configurations for NR BS, Nokia, Nokia Shanghai Bell
R4-1808794 TP to TS 38 141-1 - 4.7 Test Configurations, Ericsson
R4-1808795 TP to TS 38 141-2 - 4.8.2 Test signal Configurations, Ericsson
R4-1808973 TP to TS 38.141-1: Test configurations, Huawei
R4-1808820 TP to TS 38.141-1: Test configuration(Sections 4.7), ZTE
R4-1808821 TP to TS 38.141-1: Test configurations for multi-carrier(Sections 4.8.3), ZTE
This document summarizes the way forward on test configurations signals.

## Slide 3: Way forward
  Following signals shall be used to build NR test configurations for FR1:
  For FR2 companies are encourage to further study which test signal channel should be used for test configurations, taking into account FR2 block allocation by regulators.
FR1 | For NR bands < 100 MHz | 5 MHz, 15 kHz SCS If this channel bandwidth is not supported, the narrowest supported CBW and the smallest SCS shall be used.
 | For NR bands ≥ 100 MHz | 20 MHz, 15 kHz SCS If this channel bandwidth is not supported, the narrowest supported CBW and the smallest SCS shall be used.