## Slide 1: 3GPP 5G/NR status Dec-16 STATUS
RAN5#74 R5-171265
Athens, Greece, 13-17 Feb 2017
Source: Ericsson
Document for: Information

## Slide 2: Introduction
At RAN5#73 it was agreed to create an agenda item for status updates and early discussions on RAN5 testing aspects for 5G/NR
The purpose of this document is to provide:
  3GPP WG status - Dec-16
  Brief overview of the 5G / NR architecture, interfaces and functions
  Initial list of RAN5 discussion topics for 5G / NR
Note! The description of 5G / NR in this document is based on current draft version of TRs and is subjected to change pending development of TRs and TSs in 3GPP working groups.

## Slide 3
TS 22.261:
“Unlike previous 3GPP systems that attempted to provide a 'one size fits all' system, the 5G system is expected to be able to provide optimized support for a variety of different services, different traffic loads, and different end user communities.”

5G system capabilities:
  Flexible, scalable assignment of network resources both for access and core
  Example: Network slicing, Diverse mobility management, Multiple access technologies, …see TS 22.261 for details
5G system KPIs:
  latency, reliability and throughput
5G system – What is it about?

## Slide 4: 3GPP WG status - Dec-16 RAN#74 Report to SA#74 (SP-160954):

## Slide 5: 3GPP WG status - Dec-16 endorsed terminology (RP‑162518):
Note!
The current document use the terminology as used in the TRs published Jan-17. This mean that the terminology may differ from the terminology endorsed at RAN#74 in RP-162518.

## Slide 6: 3GPP WORK PLAN 5G/NR
3GPP Rel-14 studies related to RAN5 testing scope
  SA2 - Study on Architecture and Security for next Generation System
    Status: 100% (Dec-16), Specs: TR 23.799
  SA3 - Study on Architecture and Security for next Generation System
    Status: 45% (Dec-16, target Mar-17), Specs: TR 33.899
  RP - Study on Scenarios and Requirements for Next Generation Access Technologies
    Status Dec-16: 100%, Specs TR 38.xxx, see next slide
  RAN1 - Study on New Radio (NR) Access Technology (RAN1)
    status 55% (Dec-16, target Mar-17), Specs: TR 38.801, TR 38.912 and TR 38.802:
3GPP Rel-15 Work Items
  SA2 - 5G System - Phase 1
    Status 0% (Dec-16, target Dec-17), Specs: TS 23.501, TS 23.502
  SA1 - New Services and Markets Technology Enablers (SMARTER)
    Status 75% (Dec-16, target Mar-17), Specs: TS 22.261
  Further 5G / NR work items to come…..

## Slide 7: TRs 5G / NR (Jan-17)
Spec Number | Title
TR 33.899 v14.1.0 (SA3) | Study on the security aspects of the next generation system
TR 38.801 v1.0.0 (R3) | Study on New Radio Access Technology: Radio Access Architecture and Interfaces
TR 38.802 v1.1.0 (R1) | Study on New Radio Access Technology Physical Layer Aspects
TR 38.803 v1.1.0 (R4) | TR for Study on New Radio Access Technology: RF and co-existence aspects
TR 38.804 v0.4.0 (R2) | TR for Study on New Radio Access Technology Radio Interface Protocol Aspects
TR 38.805 v.0.0.2 (RP) | Study on New Radio Access Technology: 60 GHz Unlicensed Spectrum
TR 38.900 v14.2.0 (R1) | Study on channel model for frequency spectrum above 6 GHz
TR 38.912 v0.0.2 (S2) | Study on New Radio (NR) Access Technology
TR 38.913 v14.1.0 (RP) | Study on Scenarios and Requirements for Next Generation Access Technologies

## Slide 8: TSs 5G (Jan-17)
Spec Number | Title
TS 22.261 v1.1.0 (SA1) | Service requirements for next generation new services and markets
TS 23.501 v0.1.1 (SA2) | System Architecture for the 5G System
TS 23.502 v0.1.1 (SA2) | Procedures for the 5G System

## Slide 9: TR 38.913 v14.1.0: Study on Scenarios and Requirements for Next Generation Access Technologies
Key performance indicators
Peak data rate, Peak Spectral efficiency, Bandwidth, Control plane latency, User plane latency, Latency for infrequent small packets, Mobility interruption time, Inter-system mobility, Reliability, Coverage, Extreme Coverage, UE battery life, UE energy efficiency, Cell/Transmission Point/TRxP spectral efficiency, Area traffic capacity, User experienced data rate, 5th percentile user spectrum efficiency, Connection density, Mobility, Network energy efficiency
Deployment scenarios
Indoor hotspot, Dense urban, Rural, Urban macro, High speed, Extreme long distance coverage in low density areas, Urban coverage for massive connection, Highway Scenario, Urban Grid for Connected Car, Commercial Air to Ground scenario, Light aircraft scenario, Satellite extension to Terrestrial
Testing and Conformance Requirements (clause 11)
Conformance requirements shall be defined for NR on all deployment bands
Features/components of NR shall be designed in such a way that it is feasible to define test specifications for these features/components for both UE and BS on all deployment bands
Supplementary-Service related requirements
Multimedia Broadcast/Multicast Service, Location/Positioning Service, Critical Communications services, V2X communication
Operational requirements
Spectrum, UL Link Budget, Support for wide range of services, Co-existence and interworking with legacy RATs, V2X communication, Interworking with non-3GPP systems, Easy operation and Self Organization requirements, Cost-related requirements, Energy-related requirements, Security and Privacy related requirement relevant for Radio Access, Lawful Interception, Backhaul and signalling optimization requirements, Relay requirements, High availability

## Slide 10: New RAN functions#1 (ReF: TR 38.801 v1.0.0)
Functions similar to E-UTRAN
  Transfer of user data
  Radio channel ciphering and deciphering
  Integrity protection
  Header compression
  Mobility control functions / Handover
  Inter-cell interference coordination
  Connection setup and release
Functions specific for New RAN:
  Network Slice support
    This function provides the capability for New RAN to support network slicing
  Tight Interworking with E-UTRA
    This function enables tight interworking between NR and E-UTRA by means of data flow aggregation. This function includes at least dual connectivity. Interworking with E-UTRA is supported for collocated and non-collocated site deployments.
  Multi-connectivity
    TBD: Multi-connectivity is pending to RAN2 decision.
  E-UTRA-NR handover through a New RAN interface
    This function provides means for E-UTRA-NR handover via the direct interface between an eLTE eNB and a gNB.
  Session Management
    This function provides means for the NGC to create/modify/release a context and related resources in the New RAN associated with a particular PDU session of a UE and the corresponding tunnel between the New RAN node and the UPGW.
  Load balancing
  Distribution function for NAS messages
  NAS node selection function
  Synchronization
  Radio access network sharing
  Paging
  Positioning

## Slide 11: New RAN functions#2 (ReF: TR 38.801 v1.0.0)
New RAN may also include other functions:
  Contacting UEs in inactive mode
  Direct services support (further study related with D2D, coordinate with RAN1, RAN2)
  Interworking with non-3GPP systems (e.g. WLAN)
  E-UTRA - NR handover via CN (both intra-system and inter-system, i.e. EPC-NGCN, handovers)
  E-UTRA-NR inactive mode mobility using a direct interface between an eLTE eNB and a gNB.
See TR 38.801 clause 6.2 for more details.

## Slide 12: Architecture and I/Fs #1 (ReF: TR 38.801 v1.0.0)
New RAN logical nodes:
  gNBs
    providing the NR U-plane and C-plane protocol terminations towards the UE; and/or
  eLTE eNBs
    providing the E-UTRA U-plane and C-plane protocol terminations towards the UE.
NGC Next Generation Core NG-CP Next Generation Control Plane
UPGW User Plane Gateway gNB Next Generation Node B eLTE eNB Evolution of eNB that supports connectivity to EPC and NGC

## Slide 13: Architecture and I/Fs #2 (ReF: TR 38.801 v1.0.0)
RAN-CN interface options:
  Option 2: gNB is connected to the NGC
  Options 3/3A: eNB is connected to the EPC with Non-standalone NR. The NR user plane connection to the EPC goes via the LTE eNB (Option 3) or directly (Option 3A)

## Slide 14: Architecture and I/Fs #3 (ReF: TR 38.801 v1.0.0)
  Options 4/4A: gNB is connected to the NGC with Non-standalone E-UTRA. The E-UTRA user plane connection to the NGC goes via the gNB (Option 4) or directly (Option 4A)
  Option5: eLTE eNB is connected to the NGC

## Slide 15: Architecture and I/Fs #4 (ReF: TR 38.801 v1.0.0)
  Options 7/7A: The eLTE eNB is connected to the NGC with Non-standalone NR. The NR user plane connection to the NGC goes via the eLTE eNB (Option 7) or directly (Option 7A)

## Slide 16: New RAN operation (ReF: TR 38.801 v1.0.0)
Initial UE Access
  UE connection request -> New RAN -> NGC -> initial UE context -> Idle-to Active transition
PDU Session Management
  PDU session Setup, Modification, Release (NG CP over the NG-C interface)
Intra-system Mobility (NGC)
  intra RAT: gNB <-> gNB and eLTE eNB <-> eLTE eNB
  inter-RAT: eLTE-eNB <-> gNB
Inter-system Mobility (EPC <->NGC)
  Inter-RAT handover with E-UTRA

## Slide 17: RAN logical architecture for NR (ReF: TR 38.801 v1.0.0)
To meet the demands of next generation networks (e.g. wrt flexibility, use-case adaptation, real-time performance optimization, enable NFV/SDN) NG will introduce concepts such as
  Flexible functional split of Layer 2 and Layer 1 of radio interface
  UP-CP separation

## Slide 18: NR Physical Layer Aspects (ReF: TR 38.802 v1.1.0)
Duplexing
  FDD operation on a paired spectrum, different transmission directions in either part of a paired spectrum
  TDD operation on an unpaired spectrum, transmission direction of time resources static or dynamically changed
  DL and UL transmission directions dynamically assigned (at least for data)
Numerologies and frame structure
  Multiple numerologies are supported
  1 ms fixed subframe duration and 10ms frame length
  Scalable numerology 15kHz to 480kHz subcarrier spacing
  Resource element (RE) = one subcarrier and one symbol
  Slot = 7 or 14 OFDM symbols (subcarrier spacing of up to 60kHz), 14 OFDM symbols (subcarrier spacing > 60kHz).
  Data transmission can be scheduled to span one or multiple slots.
LTE-NR Co-existence
Carrier Aggregation / Dual Connectivity

## Slide 19: RAN NR RF and co-existence aspects (ReF: TR 38.803 v0.4.0)
RAN4 TR 38.803 covers:
  Co-existence simulations, RF feasibility, Regulatory aspect, RRM aspects
  Testability
    Testability of RRM requirements on low frequency bands (below 6GHz)
      RRM testing can generally be performed using the antenna connectors and following similar approaches as are applicable for E-UTRA.
      For some specific features of NR such as beamforming, over the air tests may be considered (reuse the tests developed for high frequency bands to avoid the need to develop both OTA and conducted tests for beam based measurements).
    Testability of RRM requirements on high frequency bands (e.g. mm-wave)
      Conducted antenna connectors are assumed not to be available.
      Performing conducted tests using an intermediate frequency (IF) has been evaluated (TR 38.803, clause 10.1.3), but current assumption is that Over the air (OTA) testing is needed for testing on high frequency bands

## Slide 20: RAN5 5G/NR DISCUSSION topics
Item# | Status | RAN5 5G/NR topics | Assumptions / Comments
1 | Open | RAN5 5G/NR test specification numbering/structure | To be part of new 3GPP 38 specification series “Radio technology beyond LTE”. Could be similar TS specification structure as for E-UTRA (38.508, 38.521-x, 38.523-x + 38 TRs, position to remain in 37-series)
2 | Open | Conformance testing for bands < 6 GHz | Antenna connector can be used (i.e. same as for E-UTRA today)
3 | Open | Conformance testing for bands >6 GHz; Band independent test cases | For multi-band devices that supports bands below 6 GHz the antenna connector can be used for band independent test cases (i.e. same as for E-UTRA today)
4 | Open | Conformance testing for bands >6 GHz; Band dependent test cases | Will require OTA testing
5 | Open | Test Control (TC) physical interface | - Preferable using the same physical interface under test (as for E-UTRA today) - Other options if deemed necessary: specific electrical or an intermediate frequency interface?
6 | Open | Deployment Scenarios priority for conformance testing | TBD based on industry priority for deployment scenarios
7 |  | <Further items to be added as identified> |