## Slide 1: Proposal to Optimize Test Execution for E-UTRAN RF CA test cases
Mohammad Omar Farooq
Intel® Mobile Certification Lab

## Slide 2: RF CA Test Cases- Test Execution Time Facts
CA band combinations are growing in number in 3GPP
Each wireless products are supporting more CA band combinations and it is growing as well.
Test execution time for TS 36.521-1 section 7.x is increasing for wireless devices with more CA combinations supported with multiple configurations. Example: A product may support 2CA, 3CA, 4CA and 5CA all types (Inter, Intra and Contiguous)
Initial certification test execution time and cost is increasing with current 5CA (and more to come in future).

## Slide 3: Proposal
If the higher CA Combo includes lower CA Combo and the test requirements are same or tighter, then the lower combo can be skipped for testing. PCC and SCC always swap for all CA test cases so all subset combinations will be tested as required. Example: If we consider test execution time for 7.6.2A.x approximately “X” hrs (X=6hrs for example) per unique band:
It can be one time execution of CA_2A-2A-5A-30A-66A instead of all the four supported bands. Test time (for above example) can be possibly reduced to 2/3 for a 5CA capable device.
Note: The test execution time X=6hrs is hypothetical not exactly related to any product. We are considering it a typical number to analyze the issue.
Proposed Optimization
CA_2A-2A-5A-30A-66A (24hrs)
CA_2A-5A (12hrs)
CA_2A-5A-30A (18 hrs)
CA_2A-2A-5A-30A (18hrs)
CA_2A-2A-5A-30A-66A (24hrs)
Total time 72hrs

## Slide 4: Test Time Example 7.6.2A.x
Set#1
CA_2A-4A (12hrs)
CA_2A-4A-5A (18hrs)
CA_2A-4A-5A-12A (24hrs)
Total time for Set#1 = 54hrs
Set#2
CA_5B-30A-66A (18hrs)
CA_5B-30A-66A-66A (18hrs)
Total time for Set#1 = 36hrs
Set#3
CA_2A-5A (12hrs)
CA_2A-5A-30A (18hrs)
CA_2A-2A-5A-30A (18hrs)
CA_2A-2A-5A-30A-66A (24hrs)
Total time for Set#1 = 72hrs
Set#4
CA_2A-12A (12hrs)
CA_12A-30A (12hrs)
CA_30A-66A (12hrs)
CA_2A-2A-12A (12hrs)
CA_2A-12A-30A (18hrs)
CA_2A-2A-12A-30A (18hrs)
CA_2A-2A-12A-30A-66A (24hrs)
Total time for Set#4 = 108 hours
Total 270hrs
Total
(24X3)hrs + 18hrs =90hrs
Proposed Optimization
Up to 2/3 reduction test execution time

## Slide 5: Proposal
Note: This concept of optimization is already taken for chapters 8 and 9 (performance test cases) , so further investigation can be considered for chapter 7.x test cases.

## Slide 6
Question?