## Slide 1: Way forward on R18 IDC Work Item
CMCC, Xiaomi
3GPP TSG-RAN5 Meeting #104 R5-245187
Maastricht, NL, Aug 19th - Aug 23th, 2024

## Slide 2: Introduction of “autonomousDenialParameters” for IDC new feature in core spec
Observation 1.1: autonomousDenialParameters is configured by the network to allow UE to deny UL transmission slot within the cell group fewer than the autonomousDenialSlots
Observation 1.2: The autonomousDenialValidity is initiated from upper bound of the first deny slot.
autonomousDenialParameters
TP for UL slot autonomous Denial

## Slide 3: Introduction of “FDM solution” for IDC new feature in core spec
Observation 2.1: If the idc-FDM-AssistanceConfig is configured, the UE did not transmit a UEAssistanceInformation message, UE transmits UEAssistanceInformation message.
Observation 2.2: If the idc-FDM-AssistanceConfig is configured, the UE transmits a UEAssistanceInformation message before, but the the current IDC information is different from the one reported previously, UE transmits UEAssistanceInformation message.
Observation 2.3: The FDM solution is applicable to both CA and NR-DC.
FDM solution
TP for FDM solution

## Slide 4: Introduction of “TDM solution” for IDC new feature in core spec
Observation 3.1: The procedure for TDM is the same as FDM, but the TDM shall be configured together with FDM configuration or the FDM configuration is configured previously.
Observation 3.2: The TDM solution is applicable to both CA and NR-DC.
TDM solution
TP for TDM solution

## Slide 5: Way forward for the IDC Work Item
Proposal 1: RAN5 agrees the initial WP, which is available in R5-244514.

## Slide 6: Thank you!