## Slide 1
Qualcomm
3GPP TSG-RAN5 Meeting #105
Orlando, USA, 18th Nov 2024 – 22nd Nov 2024
AI ML Conformance Call Flow
R5-246542

## Slide 2
==
Challenge(s) exists on conformance testing of LCM of AI ML from UE’s initial activation and starting configuration to effectively test core requirements to prove gains in performance in a reliable and repeatable way.
This Proposal aims to introduce a call flow which might be adaptable to various needs of AI ML Testability and might be able to contain some aspects of design in RAN5.
In this proposal we have examined the UE Sided Beam Management Testability i.e one sided model, but other features can be similarly adapted which may need 2 sided models ex- CSI Compression.
DISCLAIMER – Due to the dynamic nature of discussions within various core groups, this discussion\proposal should not be regarded as RAN5 feedback for any other core group or referenced in any feature discussions within core groups.
As per RP-234039 from RP#102@Dec 2023, in the WID of R19 WI “NR_AIML_Air”, for the “Testability and interoperability” topic, RAN5 aspects related to testability and interoperability to be addressed on a request basis.
RAN5 has initiated a dedicated agenda on AI ML testability aspects with an effort to help core groups with areas of RAN5 expertise.
Problem
Notes: Building Blocks – Code translating Specs into excel

## Slide 3
LCM of AI ML Model as defined in 3GPP - Info Only
3GPP- Ref TR 38.843 Fig 4.4-1 – Under Discussion in Core Groups; not all requirements under consideration
Notes: Building Blocks – Code translating Specs into excel

## Slide 4
3GPP RAN5 uses Test Mode (Test Loopback Mode or Test Functions) to put UE in a specific test mode for testing. These are specified inTS38.509 to be implemented in NAS layer for NR.
Once Core Requirements are finalized, proposal is to introduce a new Test Loop Back Mode (TLB Mode), Test Commands\Functions(s), as needed, in TS 38.509, which may –
    Activate and Deactivate UE in AI ML Test Mode to ensure UE’s is prepared with out any interference
    Define the selection of AI ML feature for UE along with initialization and trigger of assistance data to the UE’s AI ML Model for given functionality ; this can be fully defined in RAN5 to be uniform among UE and TE implementation.
    NW side AI ML Feature can be included in same Test Mode, as and when the requirements are defined.
    Any other function which is required to prepare the UE for AI ML Test Evaluation.
    The purpose of Test Mode will not be –
      To assist UE in any way shape or form which may show skewed results in UE favor
      To aid UE in controlled environment which may not be representative of real-world scenario
    An example of appropriate usage of test modes in Possible AI ML Call Flow for Conformance with UE side Beam Management Case-1 is presented in Qualcomm contribution in R5-247151
Proposal – AI\ML Test Mode
Notes: Building Blocks – Code translating Specs into excel

## Slide 5
Proposal - AI\ML Possible Conformance Call Flow
DISCLAIMER – (1)Several aspect of overall call flow are FFS in core groups. (2)The details of Test Mode are currently out of scope of this discussion.
This is tentative call flow to demonstrate AI ML conformance using Test Modes
At a high level – The Test Mode can have 3 umbrella features –
  Activates the UE to be in AI ML test mode, prior to start of test
  Configures the UE for any required AI ML Feature and or side conditions
  De-Activate the UE from AI ML Test Mode at the end of the test
The order of messages and test mode commands may be decided once core groups finalize requirements.
The figure on the right is simply a representation of tentative discussions in core groups and extrapolating those with Test Mode.
Notes: Building Blocks – Code translating Specs into excel