## Slide 1
3GPP TSG RAN5#105 R5-247151
Orlando, Florida, USA Nov 18-22, 2024
Agenda item: 4.2.3
Source: Qualcomm Inc
Title: AIML performance use cases
Document for: Information

## Slide 2
Proposal - AI\ML Possible Conformance Call Flow - same content as R5-246542
DISCLAIMER – (1)Several aspect of overall call flow are FFS in core groups. (2)The details of Test Mode are currently out of scope of this discussion.
This is tentative call flow to demonstrate AI ML conformance using Test Modes
At a high level – The Test Mode can have 3 umbrella features –
  Activates the UE to be in AI ML test mode, prior to start of test
  Configures the UE for any required AI ML Feature and or side conditions
  De-Activate the UE from AI ML Test Mode at the end of the test
The order of messages and test mode commands may be decided once core groups finalize requirements.
The figure on the right is simply a representation of tentative discussions in core groups and extrapolating those with Test Mode.
Notes: Building Blocks – Code translating Specs into excel

## Slide 3: Current AIML performance usecases
DISCLAIMER – Several aspects of overall Core & Performance requirement are FFS in core groups
Beam Management
  Main focus of the WI in RAN4
  Content intended for RRM spec 38.133. FR2 only at this time.
Positioning accuracy enhancements
  Very few aspects discussed by RAN4 at this time.
  Which spec? TBD
CSI feedback enhancement (CSI prediction)
  UE sided model
  A version of PMI reporting test case being discussed
  Throughput ratio as the KPI
  FR1 is conducted. FR2 is radiated with wireless cable approach
  Content intended for DEMOD spec 38.101-4.
CSI compression (2 sided model)
  Planned to be in TR phase

## Slide 4: BM-Case1: Spatial beam prediction wide to narrow beams
DISCLAIMER – Several aspect of overall Core & Performance requirement are FFS in core groups
Before the start of the test, AI ML test mode is activated (slide#2)
UE is configured with wide SSB beams during T1.
UE is configured to report CSI-RS narrow beams with periodic L1-RSRP reporting.
UE makes wide beam measurements and feeds them to its trained AI model.
After an inference delay, UE starts sending L1-RSRP reports with predicted fine beam measurements.
The TE evaluates several KPIs on the predicted beams, including measurement accuracy and inference delay

## Slide 5: BM-Case1: Ground Truth verification
DISCLAIMER – Several aspect of overall Core & Performance requirement are FFS in core groups
Before the start of the test, AI ML test mode is deactivated
At T1 start, the UE is configured with wide SSB beams and narrow CSI-RS beams
UE is configured to transmit periodic L1-RSRP reports for CSI-RS beams (narrow beams)
In this case, CSI-RS beams are available to the UE, so shortly after, it will measure the CSI-RS beams and start to transmit measurements in L1-RSRP report.
The TE evaluates several KPIs on the reported beams, including comparing the UE reported fine beam with actual beams configured (ground truth) to what UE predicted in earlier step with AI-ML enabled.
  Example: Prediction error should be within a RAN4 defined limit

## Slide 6: CSI Prediction (UE-sided model)
DISCLAIMER – Several aspect of overall Core & Performance requirement are FFS in core groups
Before the start of the test, AI ML test mode is activated
UE is configured with eType II codebook and fading is enabled.
UE is configured to send PMI reports.
After an inference delay, UE starts sending PMI reports containing predicted precoders.
TE configures PDSCH with UE reported precoder and does a SNR sweep to determine 90% TPUT.
At that 90% TPUT SNR, TE configures PDSCH with random precoding.
The ratio of Throughput obtained with UE reported precoder to random precoder is gamma1 which is one of the KPI to be measured.
After deactivating AI ML test mode, repeat the same procedure to compare the gamma obtained in this step vs previous step with AIML test mode activated.

## Slide 7: Summary
Observation 1: RAN4 is far from agreeing on the requirements for any of the AI ML use case.
  As part of core requirements discussion, basic framework will likely be agreed first
  Finer test case level details will happen much later during performance phase.
  Simulation link level assumptions currently agreed to investigate impact of measurements error on prediction accuracy
Proposal1: For each of the AIML performance use case verification, UE test function is needed to activate/deactivate AIML functionality in the DUT.
Proposal2: RAN5 can use its MU/TT expertise to provide TT analysis for the initial set of parameters being considered by RAN4 to see the feasibility of those params. Especially the fading aspects which will be new for BM cases.