## Slide 1: TTCN-3: NR UL Grant Allocation
R5w190013 - Initial UL Grant Allocation

## Slide 2: Initial UL Grant Allocation
TS 38.523-3 section 7.1.2.3.1.2.2 specifies the default settings for the Initial UL Grant Allocation:
TTCN selects a {LRBs IMCS} pair based on the TBS size of 256 bits and the TBS tables specified in Annex B.
The following pairs match to this TBS size. In some configuration there is a unique choice, and in others, there are different possibilities available, i.e:
          B.2.1.1: Pairs {7 0}
          B.2.1.2: Pairs {7 0}
          B.2.1.3: Pairs {1 12} {2 6}
          B.2.1.4: Pairs {2 6} {3 4}
          B.2.1.5: Pairs {1 13} {4 3} {5 2}
Currently, in case of different possibilities, TTCN selects the {LRBs IMCS} pair with minimum number of PRBs.
7.1.2.3.1.2.1 Grant allocation by RACH procedure
The UE gets assigned an uplink grant by the Random Access Response message being configured at the SS: Per default an UL grant of 256 bits is configured by TTCN.

## Slide 3: UL Grant Allocation: Observations
Open issues:
  During the RACH procedure UL Grant can be configured with different pairs of {LRBs IMCS}, some of them lead to a non-robust signal, especially in OTA environment.
  Initial UL Grant allocation for RAR uses a single UL Grant, which means there is only one reception opportunity for a not yet trained receiver.
  For UL Grant allocation, the default configuration and test case specific selection criteria differ.
    Shall this be harmonized? Or should TTCN have different criteria for the algorithms to select {LRBs IMCS} pairs?
      DL Grant allocation in automatic mode
      UL Grant allocation by SR for the default configuration during preamble.
      UL Grant allocation for type 2, 3, 4.

## Slide 4: UL Grant Allocation: Proposal I
Proposal: To define the selection criteria for {LRBs IMCS} which leads to a robust signal, i.e. selecting a low IMCS.
For instance: IMCS <= 9, this value guarantees a QPSK signal.

## Slide 5: Initial UL Grant allocation criteria for RAR: Proposal II
As per TS 38.523-3 clause 7.1.2.3.1.2.1: Grant allocation for RACH procedure For the Random Access Response message, the UE gets assigned an uplink grant configured by the SS. Per default, TTCN configures an UL grant of 256 bits. It’s proposed that – for a given TBS size – the following rules shall apply for selection of Number of PRBs and Modulation Code Scheme index:
  >> If there is a unique {LRBs IMCS} pair, TTCN shall select the values of that pair.
  >>Else in case that a given TBS allows for several {LRBs IMCS} pairs, TTCN shall identify those pairs with IMCS <= 9 = ImaxMCS , and among them, select the pair(s) with minimum number of NPRBS. Should still more than one pair (i.e. with same NPRBS) be eligible, then the one with minimum IMCS shall finally be selected.
  Example: a given TBS size of 256 bits
    B.2.1.3: Pairs {1 12} {2 6}
    B.2.1.4: Pairs {2 6} {3 4}
    B.2.1.5: Pairs {1 13} {4 3} {5 2}
    B.2.2.3: Pairs {2 3} {3 2}
    B.2.3.2: Pairs {2 6} {3 4} {15 0}
    B.2.3.1: Pairs {1 13} {4 3} {5 2} {17 0}
38.523-3 Annex B.2 | ImaxMCS
B.2.1.X Uplink TBS using MCS index table 5.1.3.1-1 | 9
B.2.2.X Uplink TBS using MCS index table 5.1.3.1-2 | 4
B.2.3.X Uplink TBS using MCS index table 6.1.4.1-1 | 9