## Slide 1: FR2 NR TT Way Forward update
3GPP TSG-RAN WG5 Meeting #82
Athens, Greece, 25th Feb – 1st Mar 2019
R5-191517r4
Telecom Italia, Orange, CMCC, DISH, Vodafone, AT&T, China Unicom, Qualcomm, Ericsson, Verizon

## Slide 2: Background
At RAN5 5G-AH#3 New FR2 MU values for IFF method introduced in R5-186344
At RAN5#81 several contributions regarding TT are presented:
  R5-186888: proposing TT = 0 and highlight Network coverage impact
  R5-187576: defining upper bound for TTs (TT = 2.1 dB)
  R5-187568: proposing TT = 0.65xMU
  R5-187235: proposing basically TT = 0.82xMU
At RAN5 RAN5#81 a WF for FR2 in TS 38.521-2 is agreed in R5-188058 and a MU update in R5-188224 and R5-188225
At RAN RAN5 5G-AH#4 MU values are updated in TS 38.903 and Spherical Coverage MU values are introduced in R5-190576
At RAN5#82 several contributions regarding TT spherical coverage test cases are presented:
  R5-191727 and R5-191836: proposing TT = 0.65xMU
  R5-191956: proposing TT = 2 dB Upper bound

## Slide 3: Agreed FR2 WF TS 38.521-2
Except the FFS and empty items, the proposed FR2 TT Values are included in the spreadsheet file, based on the following assumption:
TTs shall be defined case by case
TT = 0.65 * MU (the upper bound of MU value used for TT calculation is 5.5 dB, 0.65 upper bound TT/MU ratio). Applies to following Test Cases:
    Min Peak EIRP
    Max TRP
    Reference Sensitivity
    ACLR and SEM
TT = 0.45 MU (the upper bound of MU value used for TT calculation is 4.5 dB) for Min EIRP at 50t%-tile CDF
TT = 0.4 MU (the upper bound of MU value used for TT calculation is 5 dB) for EIS spherical coverage
TT = 0.50 * MU (the upper bound of MU value used for TT calculation is 0.01ppm , 0.5 upper bound TT/MU ratio) Applies to following Test Cases:
    Frequency error
Since TT have dependency from MU, no TT value can be defined if the corresponding MU is not finalized (business as usual).
TT values may decrease based on the experience on the field and when all parties will have more confidence in device performance
The TT values and the method to derive the TT defined until RAN5#89 (November 2020) for execution in any possible certification. At RAN5#89 the TT values shall be re-evaluated
  Required actions are specified in editor’s note in Annex F

## Slide 4: Attached Spreadsheets update
TS 38.521-2 SA FR2 TT
  New column with the agreed TT derivation method
  MU new IFF values in R5-190576 and new TT (Agreed WF in slide3)
    Spherical coverage Expanded uncertainty
    EIS Spherical coverage Expanded uncertainty
  MU IFF values updates in R5-190576
    EIRP Expanded uncertainty
    TRP Expanded uncertainty
    EIS Expanded uncertainty
  TT ACLR and SEM updates based on agreement of R5-191524