## Slide 1: Discussion on UE Relay for eMBB and IoT
China Telecom
3GPP TSG RAN Meeting #71 RP-160247
Göteborg, Sweden, March 7 - 10, 2016
Document for: discussion
Agenda Item: 10.1.1

## Slide 2: Motivation
For eMBB service, operators are facing challenges in ensuring the user experienced data rate in bad radio environment, especially in the uplink.
For IoT service,
  IoT devices require good coverage. Deployment of IoT devices, e.g. smart meter deep inside a building, is very challenging due to the bad radio environment.
  IoT devices require long battery life. Wearable devices such as glasses or watches require long battery life more than several days. Smart meters require long batter life more than 10 years.
Massive TTI bundling or repetition improves the coverage at the cost of huge resources and will reduce battery life significantly.
It is desired to have a more efficient mechanism to improve coverage and reduce power consumption and at RAN#70, a few paper have proposed the SI of UE relay for eMBB and IoT.

## Slide 3: Evaluation of UE relay for UL in eMBB
    Outdoor BS with 80% indoor UEs and 20% outdoor UEs
    Network controlled selection of UE relay
Scenarios

## Slide 4: Simulation Assumptions
Parameter | Values used for evaluation
Deployment scenarios | ISD=500m
Number of UEs | 10 active UEs/sector
Number of Tx/Rx | 1 Tx for UE, and 2 Rx for BS
UE Max Tx power | 23 dBm
UE noise figure | 9 dB
BS noise figure | 5 dB
System bandwidth | 10 MHz
Antenna pattern | TR 36.814, 3D antenna pattern downtilt = 12 degrees
Antenna gain + connector loss | Macro eNB: 17 dBi
Shadow fading Std | LOS: 4dB, NLOS: 8dB

## Slide 5: Preliminary Simulation Results
 | P0 = -82dBm | P0 = -82dBm | P0 = -73dBm | P0 = -73dBm
 | w/o UE relay | w/ UE relay | w/o UE relay | w/ UE relay
Cell average SE (bps/Hz) | 1.6306 | 1.8166 (+11.4%) | 2.0219 | 2.2624 (+38.7%)
Cell edge SE (bps/Hz) | 0.0311 | 0.0812 (+161%) | 0.0253 | 0.1494 (+491%)
Ratio of UEs using relay（%） | 0 | 22.66 | 0 | 30.55
Normalized UE Tx power | 100% | 63.7% (-36.3%) | 100% | 63.3% (-36.7%)
A mechanism using UE relay, can not only improve the coverage but also reduce the power consumption significantly.

## Slide 6: Potential Objectives
The objective of this study item is to evaluate and study the enhancement of Rel-13 ProSe to improve the uplink coverage for eMBB service and improve coverage and reduce power consumption for IoT devices.
The detailed objectives are as follows:
Identify the evaluation scenarios and methodology for UE relay functionality.
Evaluate the performance benefits of UE relay functionality in terms of coverage and power consumption.
Identify the necessary enchantments on PHY layer and protocol to sidelink and Uu air-interface.
Identify the specification impact on the above identified enhancements.