## Slide 1: Motivation for Revised WID: Enhancements on MIMO for NR
Samsung
3GPP TSG-RAN Meeting # 87-e
Electronic Meeting, March 16-19, 2020
Agenda: 13.1
RP-200438

## Slide 2: Background
The following objectives were listed in the WID for RAN4 core requirements
  Specify core requirements associated with the items specified by RAN1 [RAN4]
      Specify RRM requirements
      Identify impact on RF requirements for the reduced PAPR pi/2-BPSK DMRS and, if needed, specify RF requirements
      Identify impact on RF requirements for the uplink full power transmission and, if needed, specify RF requirements
  Both core part and performance part were discussed and progressed based on approved WI timeline.
    75% for RAN4 core requirements and 15% for performance requirements were reported as indicated in the SR shared on RAN4 reflector
  WI timeline and workplan is proposed to be changed due to the current completion level as well as unexpected COVID-19 situation
  RAN4 objectives on reduced PAPR pi/2-BPSK DMRS are also proposed to be changed based on previous RAN4 discussions.

## Slide 3: Discussions
MPR enhancement for pi/2-BPSK DMRS in FR2 was discussed. The following proposals were observed in RAN4 #94-e meeting
  R4-2000470 (Qualcomm)
    “Simulations on FR2 waveforms show that PBD waveforms requires MPR values over 1dB for certain filter coefficients. Therefore, considering PA performance variations it is recommended that the FR2 MPR tables remain unchanged”
  R4-200-517 (Nokia)
    Up to 1.5 dB more power could be achieved compared current MPR scheme however this is mostly due to relaxed specification not new DMRS
    Number of waveforms capable of achieving this 1.5 dB improvement in output power is increased when shaping is increased but it is not certain that this manifests as increased bitrate in base station receiver as spectrum starts to heavily distorted especially in case of shaping w/ [-0.3 1 0.3].
  R4-2002036 (Huawei)
    The DMRS evaluation should be focused on FR1.
    => Enhanced MPR requirements for pi/2-BPSK DMRS for FR2 is not identified, RF requirements is not needed.

## Slide 4: Proposals
Extend the completion date for both Core part and performance part
  Core part: June 2020
  Perf part: Dec 2020
Performance part shall continually discussed in Q2 in parallel with core part
For RF core requirements, limit the scope for PAPR pi/2-BPSK DMRS to FR1, i.e., revise the objectives as
  Identify impact on RF requirements for the reduced PAPR pi/2-BPSK DMRS for FR1 and, if needed, specify RF requirements