## Slide 1: Way Forward on mandatory UE support of full rate user plane integrity protection for 5G SA option 2 in Rel-16
Deutsche Telekom, BT, TIM, ORANGE, Telia Company, Telstra, KPN, Ericsson, Huawei, HiSilicon
3GPP TSG-RAN Meeting #87-e The Earth, 16. – 19. March 2020
RP-200505
288194168
288194168
327644664
56744936
281591248
258715104
258715104
258715104
258715104
258715104

## Slide 2: Background (1/2)
Currently NR UEs are only required to support a min. of 64 kbps user plane speed with integrity protection (“UP IP”); optionally the UE can indicate support of full rate UP speed with IP capability.
GSMA contacted 3GPP and informed about a vulnerability of LTE and NR security [RP-200038]
The support of UP IP is defined in the NR PDCP layer and technically under responsibility of RAN2
The device capability to support full rate UP IP is defined on the NAS protocol and under CT1 responsibility.
SA3 is the responsible group for defining the 3GPP security framework and detailed requirements.

## Slide 3: Background (2/2)
Since summer last year there has been LS exchange between RAN2 and SA3 on the matter of full rate UP IP
In a recent LS exchange involving RAN2 and SA3 [R2-1902700] indicated that (underlined added by co-signers for clarification):
  the network should avoid the situation where the UE maximum supported data rate - for which UP IP can be guaranteed - is exceeded
  that UE behaviour on exceeding the maximum supported data rate for integrity protection will be left to UE implementation

## Slide 4: Way forward
The enhanced security of the 5G system is essential for the commercialization of this new technology aiming to provide a wide range of use cases.
Based on the discussions in RAN#87e so far, as compromise - while still enabling enhanced security for new 5G use cases - the following is proposed:
3GPP RAN/SA#87e to mandate the support of full rate user plane integrity protection (UP IP) from Rel-16 onwards for all 5GC-capable UEs which support Standalone Architecture Options 2.