## Slide 1
3GPP TSG RAN WG1 #108-e R1-2202554
e-Meeting, February 21st – March 3rd, 2022
Agenda item : 8.16.1
Source : Samsung, Ericsson, Nokia, NSB, ZTE, Intel, Verizon, AT&T, KDDI,
NTT DOCOMO, LG Uplus, KT Corporation, SKT
Title : Proposal on UE Feature for Rel-17 Unified TCI
Document for : Discussion and Decision

## Slide 2: Proposal |
A UE that supports Rel-17 TCI framework supports at least:
  [2/4] activated TCI states per CC and DCI-based beam indication (both with and without DL assignment)
    For intra-cell and inter-cell beam management
  Inter-cell beam measurement/reporting
    K=4 is at least supported
    TBD: Whether Nmax=1 or Nmax=2 is at least supported
Strive to avoid duplicated functionality for the “counting” features, e.g. if a UE supports N TCI states for intra-cell, it should support N for inter-cell
According to RAN2 guidance features “per-BandCombination” and “per-Band-of-a-BandCombination” should be minimized.
  For features related to the Rel-17 TCI, the starting point could be ‘per band’