## Slide 1: Way Forward on ECCE to EREG Mapping
LG Electronics, Panasonic, CATT, NTT DOCOMO, New Postcom, Huawei, HiSilicon, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell
R1-125285
3GPP TSG RAN WG1 Meeting #71
New Orleans, USA, 12th – 16th November 2012
Agenda item: 6.2.3.1
Document for: Decision

## Slide 2: Proposal
An aggregation level L candidate consists of L consecutive ECCEs.
For localized EPDCCH,
  ECCE indices are numbered first in the PRB pair.
For distributed EPDCCH,
  When the EPDCCH set has 8 PRB pairs and an ECCE is formed by 4 EREGs,
    a candidate with aggregation level larger than 1 spans all the 8 PRB pairs.

## Slide 3: Proposal
For distributed EPDCCH,
  ECCE numbering
    Alt A: ECCE indices are numbered first within the EREG group.
    Alt B: ECCE indices are numbered across the EREG groups.
  ECCE mapping when the set contains 8 PRB pairs and an ECCE consists of 4 EREGs
    Alt X: An ECCE is mapped to PRB pairs #{0, 1, 2, 3} or #{4, 5, 6, 7}.
    Alt Y: An ECCE is mapped to PRB pairs #{0, 2, 4, 6} or #{1, 3, 5, 7}.
    Note: The selected 8 PRB pairs are re-indexed in an ascending order of the frequency domain location.