## Slide 1: Way forward on soft buffer handling
Samsung, CMCC, ITRI, New Postcom, Panasonic, ZTE
3GPP TSG RAN WG1 #71 R1-125306
New Orleans, USA, November 13 – 17, 2012 Agenda item: 6.2.1.1

## Slide 2: Proposals
Confirm the WA as agreement, i.e.
  The rate matching procedure in TS 36.212 is kept unchanged except the following:
    MDL_HARQ is the maximum number of DL HARQ processes defined in Table 7-1 in TS 36.213 for the DL-reference UL/DL configuration of the serving cell

## Slide 3: Proposals
The Rel-10 operation of storing soft channel bits in TS 36.213 is kept unchanged except
  MDL_HARQ is the maximum number of DL HARQ processes defined in Table 7-1 in TS 36.213 for the DL-reference UL/DL configuration of the serving cell

## Slide 4: Annex: Storing soft channel bits
For each serving cell, for at least KMIMO *min(MDL_HARQ, Mlimit) transport blocks, upon decoding failure of a code block of a transport block, the UE shall store at least nSB received soft channel bits for the code block, where
  MDL_HARQ is the maximum number of DL HARQ processes defined in Table 7-1 in TS 36.213 for the DL-reference UL/DL configuration of the serving cell
  Other parameters reuse Rel-10 definitions for the serving cell