## Slide 1: Way Forward on CSI Measurements for eIMTA Support
Intel, Ericsson, CATT
R1-134916
3GPP TSG RAN WG1 Meeting #74bis
Guangzhou, China, 7th – 11th October 2013 Agenda item: 7.2.1.1.3
Document for: Discussion and Decision

## Slide 2: Proposal
For each serving cell, Rel. 10 CSI subframe measurement set mechanism is reused for eIMTA support
In TM10,
  A UE can be configured with two CSI-IM resource configurations for a single CSI process
  Restriction that CSI IM configuration is a part of ZP CSI-RS is removed