## Slide 1: Way Forward on Discovery Signal Design and Network Assistance
NTT DOCOMO, Huawei, HiSilicon, Samsung, Sony, Sharp, ZTE, LG Electronics, Hitachi, ETRI, MediaTek
R1-141859
3GPP TSG RAN WG1 #76bis
Shenzhen, China, 31th March – 4th April 2014
Agenda item 7.2.4.2.2

## Slide 2: Background
CSI-RS is a good candidate as discovery RS
  Large number of orthogonal configurations, i.e., high cell multiplexing capability
  Distinguishability of transmission points (e.g., sharing same physical cell ID)
  Less legacy UE impact
  Accurate RSRP measurement performance in SCE scenario

## Slide 3: Proposal
In Rel. 12 discovery procedure, UE can assume transmission of CSI-RS in addition to PSS
  CSI-RS can be used for cell/transmission point identification and for RSRP measurement
  FFS whether UE can assume transmission of signal(s) other than PSS and CSI-RS in Rel. 12 discovery procedure

## Slide 4: Proposal
Network assistance related to discovery RS configuration information is provided to UEs for Rel. 12 discovery procedure
  Discovery RS configuration information includes at least:
    Time/frequency resource configuration
    Scrambling ID(s) of signals transmitted for Rel. 12 discovery procedure
    QCL information between signals transmitted for Rel. 12 discovery procedure

## Slide 5: Proposal
Support CSI-RS based RSRP/RSRQ measurement and reporting
  FFS between following options
    Option #1: CSI-RS based RSRP measurement is specified only for the case that measurement bandwidth is equal to or larger than 5 MHz
    Option #2: New relaxed RAN4 requirement is defined for CSI-RS based RSRP measurement using 6 and 15 RBs
    Option #3: Some enhancement of CSI-RS to meet current RAN4 requirement even in case of 6 RBs is introduced
  RSRQ = N×RSRP/RSSI. For RSSI measurement, down-select from the following alternatives
    Alt 1: RSRP + linear average of the total received power observed in OFDM symbols not including DRS within the measurement bandwidth
    Alt 2: linear average of the total received power observed in all OFDM symbols within the measurement bandwidth
    Alt 3: linear average of the total received power observed in OFDM symbols not including DRS within the measurement bandwidth
    Alt 4: legacy RSSI measurement, i.e. it requires CRS transmission in discover RS