## Slide 1: WF on resource grouping for D2D type-1 discovery
Samsung, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, LGE
3GPP TSG RAN WG1 #77 R1-142644
Seoul, Korea A.I 6.2.5.2.4
May 19th – May 23rd, 2014

## Slide 2: Background
In RAN1 #76bis, following options were considered for WAN protection
  Power control
  RSRP measurement based resource selection restriction (resource grouping)
  Guard band between WAN and D2D resources
  power boosting of WAN transmission

## Slide 3: Proposal
  RSRP based resource grouping is supported for type-1 discovery
  There are two groups within a discovery signal transmission resource pool
  Different subframes are assigned to each group
  Group is selected by a UE for discovery signal transmission based on UE RSRP measurement or DL path-loss
  Resources for each group and RSRP threshold (or DL Path-loss threshold) are configured by the network