## Slide 1: WF on CSI enhancement for NAICS
NTT DOCOMO, ALU, ASB, Huawei, HiSi, LG, MediaTek, Qualcomm, Samsung, Verizon, CMCC
R1-142682
3GPP TSG RAN WG1 #77
Seoul, Korea, 19th – 23rd May 2014
Agenda item 6.2.6.2

## Slide 2: Background
At the last RAN1 meeting, CSI enhancement for Rel.12 NAICS was discussed and the following was observed.
  CSI enhancements for Rel-12 NAICS receiver should be further studied until RAN1 #77 meeting, focusing on the following options
    Option 1: A single CSI feedback for NAICS
      Option 1-1: CSI is derived after canceling/suppressing interference
        Cancelation/suppression is assumed to use Rel-12 NAICS functionality, including interference channel estimation
        CSI calculation can be derived based on CRS, IMR, CSI-RS, and PDSCH
      Option 1-2: CSI is derived after canceling/suppressing interference
        Cancelation/suppression is assumed to use Rel-12 NAICS functionality, including interference channel estimation and blind detection
        CSI calculation can be derived based on CRS, IMR, CSI-RS, and PDSCH
      Option 1-3: CSI is derived without considering Rel-12 NAICS functionality (e.g. CSI after MMSE-IRC)
    Option 2: Multiple CSI feedback for NAICS
      Each CSI is derived based on different interference hypothesis

## Slide 3: Proposal
Observation: the following CSI enhancement for NAICS were proposed.
  Extending CSI reference resource definition to the resource allocation of the scheduled PDSCH
  Additional feedback to assist the network with assessing the benefit of network assistance signaling and making reconfigurations to NAICS UE.
  NAICS CQI with a fixed modulation assumption of interference signal
  Aperiodic CSI-IMR configuration
  Configuration of interference averaging interval for CSI calculation by network side
  NAICS CSI calculated based on interference observed over a CSI-IM
  Multiple CSI feedback assuming different receiver type
  Modification of CQI definition
Among the above proposals, consensus on the benefits of CSI enhancement has not been yet reached
Proposal: In Rel-12, there is no change to the current CQI definition for NAICS CSI reporting.
  Note that the UE would take into account any NAICS gains into the CQI derivation depending on UE implementation and it is up to RAN4 whether a new test case is required.