## Slide 1: WF on PHR triggerer
Broadcom, InterDigital
R1-142732
3GPP TSG RAN WG1 #77
Seoul, Korea, 19th – 23rd May 2014
Agenda item 6.2.4

## Slide 2: Background
RAN2 agreement made in last meeting:
  Pathloss change, P-MPR change, and SCell activation triggers PHR for both MAC entities.
  Periodic, and Reconfiguration triggers PHR to corresponding MAC entity.
  PHR prohibit timer is started when a MAC entity sends PHR.
Additionally 36.321, section 5.4.6 says:
  NOTE: The UE should avoid triggering a PHR when the required power backoff due to power management decreases only temporarily (e.g. for up to a few tens of milliseconds) and it should avoid reflecting such temporary decrease in the values of PCMAX,c/PH when a PHR is triggered by other triggering conditions.
Thus, PHR of both SG are NOT transmitted periodically nor often
None of these trigger when UE becomes power limited as a result of the other eNB increasing its grant

## Slide 3: Proposal
PHR should be triggered when UE becomes power-limited due to independent scheduling decisions between MeNB and SeNB
  RAN1 to define the exact condition
  Send LS to RAN2 after condition is defined