## Slide 1: Discussion on soft buffer size for Rel-12 new UE categories
Huawei,Hisilicon
3GPP TSG RAN WG1 Meeting #80bis R1-152175
Belgrade, Serbia, 20 - 24th April, 2015
Agenda item 7.1

## Slide 2: Background
It is proposed to introduce Rel-12 UE category 15 and 16 to support the following application scenarios
  The Maximum number of DL-SCH transport block bits received within a TTI (peak data rate) and Total number of soft channel bits are directly calculated from the corresponding scenarios
  The scenario with maximum achievable peak data rate (highlighted above) is used to determine the downlink PHY layer parameter values of this category, i.e,“Total number of soft channel bits”
UE DL Category | Application scenario | Maximum number of DL-SCH transport block bits received within a TTI | Total number of soft channel bits
DL Category 15 | 2CC 4*4MIMO + 1CC 2*2MIMO; | 749856 | 9084672
 | 1CC 4*4MIMO + 3CC 2*2MIMO; | 751808 | 9110016
 | 5CC 2*2 MIMO; | 753760 | 9135360
 | 2CC 4*4MIMO 256QAM; | 783264 | 9486336
 | 1CC 4*4MIMO 256QAM + 2CC 2*2MIMO 256QAM; | 783216 | 9486336
 | 4CC 2*2MIMO 256QAM; | 783168 | 9486336
 | 1CC * 2MIMO 256QAM + 4CC *2MIMO 64QAM | 798800 | 9679872
DL Category 16 | 2CC 4*4MIMO 256QAM + 1CC 2*2MIMO 256QAM; | 979056 | 11857920
 | 1CC 4*4MIMO 256QAM +3CC 2*2MIMO 256QAM; | 979008 | 11857920
 | 5CC 2*2MIMO 256QAM; | 978960 | 11857920
 | 3CC 4*4MIMO + 1CC 2*2 MIMO; | 1049408 | 12713472
 | 2CC 4*4 MIMO +3CC 2*2MIMO; | 1051360 | 12738816

## Slide 3: Soft buffer size per DL cell
By directly calculating from the scenario with maximum achievable peak data rate, the eNB assumptions on soft buffer size per DL cell are as below
  The values for other application scenarios are scaled by the supported CC and modulation type
DL Scenarios with maximum achievable peak data rata | UE category | Total number of soft channel bits | eNB encodes the transport block(s) assuming the following soft buffer size per DL cell (Ncc is the number of configured component carriers) |  |  |  | 
 |  |  | Ncc=1 | Ncc=2 | Ncc=3 | Ncc=4 | Ncc=5
4cc+2layer;  | Cat 11/12 | 7308288 | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192****
1CC * 2MIMO 256QAM + 4CC *2MIMO 64QAM | Cat 15 | 9679872 | 1935974* 3871948** 2419968*** 4839936**** | 1935974* 3871948** 2419968*** 4839936**** | 1935974* 3871948** 2419968*** 4839936**** | 1935974* 3871948** 2419968*** 4839936**** | 1935974* 3871948** 2419968*** 4839936****
2cc+4layer & 3cc+2layer; | Cat 16 | 12738816 | 1819830* 3639661** 2547763*** 5095526**** | 1819830* 3639661** 2547763*** 5095526**** | 1819830* 3639661** 2547763*** 5095526**** | 1819830* 3639661** 2547763*** 5095526**** | 1819830* 3639661** 2547763*** 5095526****
*) wo 256QAM and Maximum of 1-2 layers is supported by the UE, **) wo 256QAM and Maximum of 4-8 layers is supported by the UE
***) w 256QAM and maximum of 1-2 layers is supported by the UE, ****) w 256QAM and maximum of 4-8 layers is supported by the UE
* Cat 11/12 are listed as reference

## Slide 4: Analysis on the soft buffer size per DL cell
Observation
  The eNB assumption on the soft buffer size per DL cell for the same MIMO/modulation scenario is different in different UE categories, e.g,
    wo 256QAM+ 1~2 layer, 1827072 (legacy UE cat.) vs. 193597 (cat.15) vs. 1819830 (cat.16),
    w 256QAM + 1~2 layer, 2436096 (cat.11/12) vs. 2419968(cat.15) vs. 2547763 (cat. 16)
Drawbacks of the different soft buffer size per DL cell for the same MIMO/modulation scenario in different UE categories
  Mismatched eNB/UE assumption on soft buffer size per CC when an advanced UE enters a pre-release eNB network, which results in decoding failure
  Great standard efforts to describe the different soft buffer size per DL cell for each new UE category
  May impose different UE implementation for the same MIMO/modulation type

## Slide 5: Proposal on soft buffer size per DL cell
For categories 15 and 16, aligning the eNB assumption on soft buffer size for each DL cell for the same MIMO/modulation scenario to legacy UE category , i.e, Cat. 11/12
Agree on the following table for “Total number of soft channel bits "and eNB assumption on soft buffer size per DL cell for categories 15 and 16
Merits
  Backward compatible: No mismatch on soft buffer size per DL cell between eNB and UE for the same MIMO/modulation scenario
  Forward compatible: No need to describe the soft buffer size per DL cell for each new UE category
  Standard effort is kept minimal
DL Scenarios with maximum achievable peak data rata | UE category | Total number of soft channel bits | eNB encodes the transport block(s) assuming the following soft buffer size per DL cell (Ncc is the number of configured component carriers) |  |  |  | 
 |  |  | Ncc=1 | Ncc=2 | Ncc=3 | Ncc=4 | Ncc=5
4cc+2layer;  | Cat 11,12 | 7308288 | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192****
1CC * 2MIMO 256QAM + 4CC *2MIMO 64QAM | Cat 15 | 9744384 (9679872) | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192****
2cc+4layer & 3cc+2layer; | Cat 16 | 12789504 (12738816) | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192**** | 1827072* 3654144** 2436096*** 4872192****

## Slide 6: Proposal for the Downlink PHY parameter values for Cat. 15/16
DL UE Category | Maximum number of DL-SCH transport block bits received within a TTI | Maximum number of bits of a DL-SCH transport block received within a TTI | Total number of soft channel bits | Maximum number of supported layers for spatial multiplexing in DL
DL Category 15 | 798800 | 149776 (4 layers, 64QAM) 195816 (4 layers, 256QAM) 75376 (2 layers, 64QAM) 97896 (2 layers, 256QAM) | 9744384 | 2 or 4
DL Category 16 | 1051360 | 149776 (4 layers, 64QAM) 195816 (4 layers, 256QAM) 97896 (2 layers, 256QAM) | 12789504 | 2 or 4