## Slide 1: On the key characteristics of MUST schemes
Huawei, HiSilicon, MediaTek, Qualcomm
3GPP TSG RAN WG1 Meeting #81 R1-153685
Fukuoka, Japan, 25th – 29th May2015
Agenda Item: 6.2.7.3

## Slide 2: Background
It was encouraged by RAN1 chairman to discuss the details of the MUST schemes, and to understand the differences and commonalities among the schemes.

## Slide 3: Observation
Example of Candidate Schemes | Power ratio | Gray mapping | Adaptable label bit assignment | Superposition domain
NOMA | Needed | N | N | Linear symbol
SOMA | Needed | Y | N | Non-linear Bits
NOMA with Gray Mapping | Needed | Y | N | Linear symbol
REMA | Not needed | Y | Y | Non-linear Bits
There are at least following distinguishing characteristics among all of the candidate schemes proposed up to RAN1#81
  Whether defining a power ratio is needed between near UE and far UE
  Whether gray mapping is used at composite constellation
  Whether adaptable label bit assignment is used
  Whether superposition is operated in linear symbol domain or in non-linear bit domain

## Slide 4: Proposal
Companies are encouraged to describe at least the following characteristics of their MUST schemes:
  Whether defining a power ratio is needed between near UE and far UE
  Whether gray mapping is used at composite constellation
  Whether adaptable label bit assignment is used
  Whether superposition is operated in linear symbol domain or in non-linear bit domain