## Slide 1: Way forward on observations of system-level simulation results for PDSCH MUST
MediaTek, Huawei, HiSilicon, HTC, ITRI, CHTTL, NTT DoCoMo, Sony, ZTE
3GPP TSG RAN WG1 #83
Anaheim, USA, 16th – 20th November 2015
Agenda item: 6.2.7.1
R1-157593

## Slide 2: Proposed Observations for TR (1/2)
  For system-level simulation results using wideband scheduling for FTP traffic, assuming Release 12 EVM requirements for 64QAM
  MUST provides -3% ~ 7% performance gain in average UPT when RU is around 60%
  MUST provides -5% ~ 16% performance gain in 5%ile UPT when RU is around 60%
  MUST provides 7% ~ 15% performance gain in average UPT when RU is around 70% or higher
  MUST provides 10% ~ 30% performance gain in 5%ile UPT when RU is around 70% or higher

## Slide 3: Proposed Observations for TR (2/2)
  For system-level simulation results using subband scheduling for FTP traffic, assuming Release 12 EVM requirements for 64QAM
  MUST provides -2% ~ 4% performance gain in both average and 5%ile UPT when RU is around 60%
  MUST provides 3.6% ~ 11% performance gain in average UPT when RU is around 70% or higher
  MUST provides 6.6% ~ 26% performance gain in 5%ile UPT when RU is around 70% or higher
For full buffer, the range of performance gain is 5% ~ 18% and 10% ~ 25% for cell-average and cell edge respectively.
  In general, MUST increases system capacity as well as user experience