## Slide 1: Way forward on PUCCH for Class A
Ericsson, ZTE, Intel, ITRI, CMCC
AI: 6.2.4.3.2
3GPP TSG-RAN WG1#83 R1-157623
Anaheim, US, 16th - 20th November 2015

## Slide 2: Proposal, Class A CSI reporting
For P-CSI reporting, the UE measures and reports CSI based on a configured legacy CSI-RS resource
  Using legacy codebooks, CSI reporting modes and procedures
For A-CSI reporting, the UE measures and reports CSI based on a configured Rel.13 CSI-RS resource
  Using Rel.13 codebooks, CSI reporting modes and procedures
Note: CSI-RS resource configuration is independent for P-CSI and A-CSI but can be configured as overlapping ports to reduce total CSI-RS overhead (provided that P-CSI ports corresponds to a 1D port layout)