## Slide 1: Proposals for NB-IoT synchronization signal resource mapping
Huawei, HiSilicon, Ericsson, U-blox
R1-157750
3GPP TSG RAN WG1 #83
Anaheim, USA, November 15-22, 2015
Agenda item 6.2.6.2.1

## Slide 2: Proposals
The following resource mapping rules are complied with:
  The first 3 LTE OFDM symbols are not used by NB-PSS/NB-SSS
  NB-PSS/NB-SSS are punctured by LTE CRS
  NB-PSS/SSS are punctured by LTE CSI-RS and PRS if collision occurs
  NB-PSS/SSS occupy fixed number of OFDM symbols in each synchronization subframe
    Normal CP: NB-PSS and NB-SSS span 11 OFDM symbols and X OFDM symbols respectively in each subframe transmitting the synchronization signal
      X=11, 9, 6
      Note: The value of X may depend on the number of information bits, UE decoding complexity, decoding performance, etc.
    Extended CP if supported: NB-PSS and NB-SSS span 9 OFDM symbols and Y OFDM symbols in each subframe transmitting synchronization signal
      Y=9, 6
      Note: The value of Y may depend on the number of information bits, UE decoding complexity, decoding performance, etc.