## Slide 1: WF on SRS for eMTC
InterDigital, Panasonic, CATT, Intel
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda Item: 6.2.1.11
R1-157823

## Slide 2: Background
Agreement:
For Mode A
  Both periodic and aperiodic SRS is supported
For Mode B
  Neither aperiodic nor periodic SRS is supported
For Mode A
  Reuse existing R12 SRS configurations
  No repetition is used

## Slide 3: Proposal
For Mode A
  SRS request for A-SRS is transmitted in DCIs for UL and DL grant
  SRS is always dropped if retuning is required for PUSCH/PUCCH due to the SRS transmission
  The last symbol of PUSCH is rate-matched around if it collides with cell-specific SRS bandwidth (i.e., legacy behaviour)
  The shortened PUCCH is used in a cell-specific SRS subframe based on ackNackSRS-SimultaneousTransmission configuration signalled in MTC-SIB (i.e., legacy behaviour)
For Mode B
  The last symbol of PUSCH is punctured if it collides with cell-specific SRS to allow symbol level combining
  The shortened PUCCH is used in a cell-specific SRS subframe based on ackNackSRS-SimultaneousTransmission configuration signalled in MTC-SIB (i.e., legacy behaviour)