## Slide 1: WF on PUSCH & PDSCH Repetitions
Sony, Panasonic, …
R1-161125
3GPP TSG RAN WG1 Meeting #84
St Julian’s, Malta, 15th - 19th February 2016
Agenda item 7.2.1.2.1

## Slide 2: Proposal 1
Define a Rate Matched Block
  Rate matching is realized to the size corresponding to a Rate Matched Block
  Rate Matched Block is indicated (explicit or implicit) by NB-PDCCCH.
  Rate Matched Block can be further repeated and the number of repetition is indicated in NB-PDCCH.
    The number of repetition is a power of 2
  Note that this proposal is independent whether RV is introduced or not. See slide 4.
    For NB-PDSCH, the Rate Matched Block can occupy one or more scheduling units depending on the TBS
    For NB-PUSCH, the Rate Matched Block occupies
      One scheduling Resource Unit if RV cycling is used
      One or more scheduling Resource Units if RV cycling is not used

## Slide 3: Proposal 2
When the number of the repetition of the Rate Matched Block is 4 and more, the repetition pattern is realized by using Cyclic Subframe level repetition. Each cycle the subframe is repeated Z times
  Z= min(4, number of repetitions)

## Slide 4: Example of Rate Matched Block & Cyclic Subframe Level Repetition (No RV Cycling)
TB
Coding
Rate Match
6 subcarriers
Resource unit = 2 subframes
A
B
C
D
1 subframe
1 Resource Unit
6 subcarriers
Rate Matched Block
Repetition (8×)
A
A
A
A
B
B
B
B
C
C
C
C
D
D
D
D
Z=4
1 cycle
A
A
A
A
B
B
B
B
C
C
C
C
D
D
D
D

## Slide 5: Example of Rate Matched Block & Cyclic Subframe Level Repetition (RV Cycling)
TB
Coding
Rate Match
6 subcarriers
Resource unit = 2 subframes
A
B
C
D
1 subframe
1 Resource Unit
6 subcarriers
Rate Matched Block
Repetition (8×)
A
A
A
A
B
B
B
B
C
C
C
C
D
D
D
D
Z=4
RV1
A
A
A
A
B
B
B
B
C
C
C
C
D
D
D
D
RV1
RV2
RV2
RV1
RV2
1 cycle