## Slide 1: WF on >6GHz Channel Modeling Scenarios for Calibration
NTT DOCOMO, Nokia Networks, Samsung, …
R1-161146
3GPP TSG RAN1#84
St Julian’s, Malta, Feb. 15 - 19, 2016
Agenda Item: 7.3.5.1

## Slide 2: Proposal
The propagation scenarios defined in this WF are defined for calibrating different companies channel model implementation once the channel model is completed.
  More parameters for the scenarios might be needed depending on the development of channel model.

## Slide 3: Proposal
Details on UMi-street canyon and UMa scenarios are listed in the following table
  Other parameters are FFS.
Parameters |  | UMi – street canyon | UMa
Cell layout |  | Hexagonal grid, 19 micro sites, 3 sectors per site (ISD = 200 m) | Hexagonal grid, 19 macro sites, 3 sectors per site (ISD = 500 m)
BS antenna height (hBS) |  | 10 m | 25 m
UE location | Outdoor/indoor | Outdoor and indoor | Outdoor and indoor
 | LOS/NLOS | LOS and NLOS | LOS and NLOS
 | Height (hUE) | Same as 3D-UMi in TR 36.873 | Same as 3D-UMa in TR 36.873
Indoor UE ratio |  | 80 % | 80 %
UE mobility (horizontal plane only) |  | 3 km/h | 3 km/h
Min. BS - UE distance (2D) |  | 10 m | 35 m
UE distribution (horizontal) |  | Uniform | Uniform

## Slide 4: Proposal
Details on indoor-office scenarios are listed in the following table
  Other parameters are FFS.
Parameters |  |  | Indoor – office open office | Indoor – office mixed office
Layout | Room size (WxLxH) |  | [120mx50mx3m] | 
 | ISD |  | 20m | 
BS antenna height (hBS) |  |  | 3 m (ceiling) | 
UE location |  | LOS/NLOS | FFS | FFS
 |  | Height (hUE) | 1.0 m | 
UE mobility (horizontal plane only) |  |  | 3 km/h | 
Min. BS - UE distance (2D) |  |  | FFS | 
UE distribution (horizontal) |  |  | Uniform | 

## Slide 5: Proposal
50 m
120 m
BS
Layout of the indoor office
15 m
15 m
20 m
10 m
20 m
20 m
20 m
20 m
20 m
10 m

## Slide 6: Proposal
Details on UMi-open square scenario are listed in the following table
  Other parameters are FFS.
Parameters |  | UMi – open square
Cell layout |  | FFS
BS antenna height (hBS) |  | 10 m
UE location | Outdoor/indoor | Outdoor for UEs in open square, outdoor and indoor otherwise
 | LOS/NLOS | LOS for links between UEs and BSs in open square; LOS and NLOS for the other links
 | Height (hUE) | Same as 3D-UMi in TR 36.873
Indoor UE ratio |  | 80 % for UEs outside open square
UE mobility (horizontal plane only) |  | 3 km/h
Min. BS - UE distance (2D) |  | FFS
UE distribution (horizontal) |  | Uniform (the density of UEs inside open square can be different from that outside of open square; the density value(s) TBD)

## Slide 7: Proposal
Indoor - shopping mall
  Large multiple-story building with open ceiling in the middle. Shops are arranged along the outer wall of the building.
  BS antennas are regularly placed with ISD = 20m.
  Other details on indoor shopping mall are FFS.
40 m
100 m
Corridor
Open ceiling
Shop
10 m
20 m
20 m
20 m
20 m
10 m
10 m
10 m
20 m