## Slide 1: DMRS enhancement for V2V
CATT, LGE, Nokia Networks, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, ZTE
3GPP TSG RAN WG1 Meeting #84
St Julian’s, Malta, 15th - 19th February 2016
R1-161197

## Slide 2: Background
In RAN1 meeting #83, the followings are agreed
Confirm the baseline on SC-FDM is used for V2V transmission in each physical channel
Working assumption: Increase DMRS density to 4 symbols per 1ms with reusing PUSCH DMRS sequence in each physical sidelink channel except for PSBCH
  FFS location of DMRS
    Possible options for evaluation and further study will be discussion during this week
  FFS the number and location of DMRS in PSBCH (if PSBCH is supported)
    Possible options for evaluation and further study will be discussion if PSBCH is supported during this week
If RAN1 finds working assumption does not work, i.e. the performance cannot meet requirements for PC5 V2V at least including consideration on whether RAN1 working assumption of frequency offset is confirmed, the first priority should be given to DMRS structure with Comb (like SRS).
There should be considerations on receiver complexity when working assumption is confirmed.

## Slide 3: Observation
The performance of legacy DMRS structure is hard to meet all requirements for PC5 V2V with the assumed frequency error in some cases

## Slide 4: Proposals
DMRS sequence should be improved as comb-structure to support larger frequency shift in V2V
Option 1 of DMRS location is preferred for V2V