## Slide 1: WF on >6GHz Channel Modeling Scenarios
NTT DOCOMO, ALU, ASB, CATT, Ericsson, ETRI, Fraunhofer, Intel, InterDigital, KT, LGE, NEC, Mitsubishi, Nokia, NTT, Samsung, Sharp, Sony
R1-161228
3GPP TSG RAN1#84
St Julian’s, Malta, Feb. 15 - 19, 2016
Agenda Item: 7.3.5.1

## Slide 2: Proposal
Scenarios for >6GHz channel modeling are as follows.
  UMi – street canyon
    Urban micro cell with high (outdoor/indoor) UE density.
    BS is placed below rooftop level of surrounding buildings.
  UMi – open square
    Urban micro cell with high UE density.
      MSs in the open square are outdoor. MSs outside of the open square can be either outdoor or indoor.
    BS is placed below rooftop level of surrounding buildings.
    BS can be placed at surrounding buildings or inside of the open square, e.g., lamppost.
    Width of the open square is in the order of 50 to 100 m.
    Note: This scenario can be applicable for Stadium case.
  UMa
    Urban macro cell with high (outdoor/indoor) UE density.
    BS is placed at or above rooftop level of surrounding buildings.

## Slide 3: Proposal
Scenarios for >6GHz channel modeling are as follows (Cont.)
  Indoor – office
    Sub scenario 1 – Open office: Typical open office environment with cubicles, chairs, etc.
    Sub scenario 2 – Mixed office: Typical office environment with open cubicle areas, meeting rooms, walled offices, corridors, etc.
    We utilize common modeling methodologies and parameterization, unless separate modeling is identified as necessary.
    Following features are separately modeled.
      LOS probability
      FFS: other features
    BS is placed at ceiling.
  Indoor – shopping mall
    Large multiple-story building with open ceiling in the middle. Shops are arranged along the outer wall of the building.
    BS is placed at ceiling. Details FFS.

## Slide 4: Proposal
Following scenarios are the 1st priority.
  UMi – street canyon
  Indoor – office
Other scenarios are the 2nd priority.
  The completion of detail modeling for each 2nd priority scenario should not prevent the completion of channel model SI.
Priority of scenarios can be further discussed considering discussion in RAN plenary.