## Slide 1: WF on multiplexing of NB-PDCCH and NB-PDSCH
ZTE, …
R1-161232
3GPP TSG RAN WG1 #84 meeting
St. Julian, Malta, 15th – 19th February 2016
Agenda item 7.2.1.1.2

## Slide 2: Proposals
The resource unit of NB-PDSCH is one PRB, i.e., 12 subcarriers of 1 subframe.
  Different NB-PDSCHs are TDM
NB-PDCCH and NB-PDSCH are TDM, i.e., NB-PDSCH and other UEs’ NB-PDCCH are not in the same subframe.
An NB-PDCCH/NB-PDSCH for extended or extreme coverage UE can be transmitted over multiple scheduling windows.
  Scheduling window is a scheduling period consisting of control region followed by data region.