## Slide 1: WF on NB-CCE and NB-PDCCH search space
ZTE, …
R1-161233
3GPP TSG RAN WG1 #84 meeting
St. Julian, Malta, 15th – 19th February 2016
Agenda item 7.2.1.1.2

## Slide 2: Proposals - 1
An NB-CCE consists of 6 consecutive subcarriers in a subframe.
Max. AL = 2. When AL = 2 is used, two NB-CCEs of the same UE are in the same subframe
Repetition is only applied to AL = 2.
Within a scheduling window, the repetition of an NB-PDCCH occupies consecutive (available) subframes.
  A scheduling window is a scheduling period consisting of control region followed by data region.
For extended and extreme coverage cases, AL is fixed to 2 and an NB-PDCCH is repeated over multiple scheduling windows.
  NB-PDCCH can also be repeated within a scheduling window, and total number of repetitions is the number of repetitions across scheduling windows and the number of repetitions within a scheduling window

## Slide 3: Proposals - 2
For normal coverage case,
  Rmax is fixed to 4.
  For AL = 1, 8 candidate sets are defined.
  For AL = 2, 4 candidate sets are defined.