## Slide 1: WF on Number of Repetitions for PUCCH for eMTC
Ericsson, Nokia, ALU, ASB, Sequans, Qualcomm, MediaTek
R1-161241
3GPP TSG RAN WG1 Meeting #84
St Julian’s, Malta, 15th – 19th February 2016
Agenda item 7.1.5

## Slide 2: Background
RAN1#83 agreement:
  PUCCH resource for Msg4 uses same handling as PUCCH resource determination associated with regular PDSCH
    Same implicit derivation as regular PDSCH
    No new parameter/field dedicated to Msg4 feedback is introduced
  RRC parameter “Number of PUCCH repetitions” value range for PUCCH is according to
    {1,2,4,8} for CE Mode A, {4, 8,16,32} for CE mode B
pucch-NumRepetitionCE | Number of PUCCH repetitions | CE mode A: {1, 2, 4, 8} CE mode B: {4, 8, 16, 32} | UE specific

## Slide 3: Proposal 1
NumRepetition of PUCCH for HARQ-ACK to Msg4 is derived based on RRC parameter pucch-NumRepetitionCE
  Keep RAN1#83 agreement: No new parameter/field dedicated to Msg4 feedback is introduced
  The derivation is based on a look-up table

## Slide 4: Proposal 1 (Cont): Look-up Table
Max Number of repetitions of PUSCH in CE Mode B | “Number of PUCCH repetitions” for PUCCH in response to Msg4
192, 256 | 4
384, 512 | 8
768, 1024 | 16
1536, 2048 | 32
Max Number of repetitions of PUSCH in CE Mode A | “Number of PUCCH repetitions” for PUCCH in response to Msg4
Max number of repetitions of PUSCH = 8, actual number of repetitions of PUSCH carrying Msg 3 is either 1 or 2 | 1
Max number of repetitions of PUSCH = 8, actual number of repetitions of PUSCH carrying Msg 3 is either 4 or 8 | 2
16 | 4
32 | 8
For PRACH CE level 0 or 1
For PRACH CE level 2 or 3

## Slide 5: Proposal 2
NumRepetition of PUCCH format 1/1a/2/2a are based on RRC parameter pucch-NumRepetitionCE without introducing new RRC parameters
  NumRepetition of PUCCH format 1/1a: same as RRC parameter pucch-NumRepetitionCE
  NumRepetition of PUCCH format 2/2a: derived from RRC parameter pucch-NumRepetitionCE with an offset (e.g., the next level up in pucch-NumRepetitionCE up to the max in pucch-NumRepetitionCE)

## Slide 6: Backup
pdsch-maxNumRepetitionCEmodeA | Maximum value to indicate the set of PDSCH repetition numbers for CE mode A | {8, 16, 32}
pdsch-maxNumRepetitionCEmodeB | Maximum value to indicate the set of PDSCH repetition numbers for CE mode B | {192, 256, 384, 512, 768, 1024, 1536, 2048}